## Pen-type Visual Fault Locator (VFL)---------JW3105-Pen-type

The JW3105 Pentype VFL is specially designed for field personnel who need an efficient and economical tool for fiber tracing, fiber routing and continuity checking in optical network. It includes:

- Finding the breakpoint, poor connections, bending or cracking in fiber optic cables.

- Finding the faults of OTDR dead zone

- End-to-end visual fiber identification

### Features

- 2.5mm universal connector, for 1.25mm connectors,

FC (Male)-LC (Female) adapter can be provided on requests.

- Operates either in CW or Pulsed

- Constant output power

- Lower Battery warning

- Long battery life (up to 60 hours)

- Crash-proof and dust-proof design for laser head

- Laser case ground design prevents ESD damage

- Burning testing to ensure the reliability.

- Portable and rugged, easy to use

- Guarantee to CE standards include EMC, EMI, ROHS

#### Specifications

| Type | JW3105 Pen-type Visual Fault Finder |
| --- | --- |
| Central Wavelength | 650nm±10nm |
| Emitter Type | FP-LD |
| Output Power | 1mw, 3mw, 5mw, 10mw can be optional on customer request |
| Optical Connector | 2.5mm universal connector For 1.25mm connectors, FC (Male)-LC (Female) adapter can be provided on customer requests |
| Operating Model | Both CW and Pulse available |
| Pulse Frequency | 2~3Hz |
| Power Supply | 2 AA alkaline batteries |
| Battery Operating Time | 650nm@1mw ≥65hour 650nm@3mw ≥50hour 650nm@10mw≥15hour Test with Panasonic LR6 AA ALKALINE battery |
| Operating Temperature | -10~+45 (℃) |
| Storage Temperature | -40~+70 (℃) |
| Dimension (mm) | ￠15X180 |
| Weight | 120g(Without battery) |

#### Standard Packages

| MODEL | INCLUDES |
| --- | --- |
| JW3105 Pen-type VFL | Main unit, 2pcs Alkaline battery, Instruction Manual, Cotton swabs and Nylon Soft Carrying case. |

## Visual Fault Locator(VFL)---------JW3105

JW3105 Visual Fault Locator

is used for the measurement in single-mode or multi-mode fibers. It features a rugged design, an universal connector and an accurate measurement. The JW3105 visual fault locator easily identifies the cutting, micro-bending of the optic fiber, passes through the jacket fiber and performs an end-to-end fiber identification. Its measurement range is up to 5km. It is an ideal tool for the examination of all kinds of patch cords and ribbon or bunched pigtails in the installation and maintenance of fiber optic networks.

### Features

- Detects breaks, micro-bends even through jacketed fibers

- End-to-end visual fiber identification

- Locates faults up to 5km along the fiber.

- Mechanical fusion splice optimization

- Compact size and light weight, suitable for field testing

## Applications

Maintenance in Telecom

Maintenance CATV

Test Lab of optical fibers

Other Fiber Optic Measurements

#### Specifications

| Type | JW3105 |
| --- | --- |
| Wavelengths(nm) | 650±10nm |
| Fiber Model | SM,MM |
| Ouput Power | 1mw, 3mw,5mw, 10mw can be optional on customer request |
| Spectral Width(nm) | ≤5 |
| Emission | CW, 2Hz can be optional |
| Optical Connector | FC/ Universal 2.5mm adaptor |
| Power Supply | 2pcs AA alkaline batteries |
| Battery Operating Time | 30 hours |
| Operating Temperature(℃) | -10~+60 |
| Storage Temperature(℃) | -25~+70 |
| Dimension(mm) | 100X50X25 |
| Weight (g) | 50 |

Remark: JW3105 Pen-type VFL is available!

| Standard PackagesMODEL | INCLUDES |
| --- | --- |
| JW3105 | JW3105 Visual Fault Locator, Alkaline battery, Instruction Manual, Cotton Swabs and Protective Holster. |

# Text boxes

New in 2008