| Processor |
| --- |
| Alpha 21264 466-MHz processor |
| Cache Memory |
| 2-MB onboard cache |
| Upgradability |
| Supports upgrades of memory and hard drives |
| Standard | One CPU |
| Memory |
| Standard | 128 MB, 256 MB, 512 MB, or 1 GB (one memory kit) |
| Maximum | 2 GB (two memory kits, kits include two industry-standard DIMMs with ECC support) |
| Network Controller |
| Onboard dual 10/100 BaseT Ethernet ports |
| Expansion |
| Storage bays | Five (Diskette drive bay, CD-ROM drive bay, 5.25( x 1.6( removable media bay or 3.5( x 1( hard disk drive bay, two 3.5( x 1( hard disk drive bays) |
| PCI slots | Four slots (three 64-bit, one 32-bit) |
| Storage |
| Diskette Drive | 1.44-MB diskette drive |
| CD-ROM | 5.25( half height CD-ROM drive |
| Hard Drives | 10-GB IDE disk drive or 9.1-GB and 18.2-GB UltraSCSI disk drives available |
| Storage Controller |
| Onboard IDE controller for internal storage, PCI SCSI controller optional |
| Interfaces |
| Parallel | One bi-directional enhanced port |
| Serial | Two ports, one serial port with full-duplex asynchronous modem control and one RMS dedicated serial port with full-duplex asynchronous modem control |
| Keyboard | One PS/2-style port |
| Mouse | One port |
| Power Supplies |
| 300W (120/240V, 60/50 Hz ) |
| Manageability |
| Software features for advanced server and network management, including ServerWORKS™ Manager ServerWORKS workgroup administrator ServerWORKS Manager application SNMP agents to manage SCO UNIX, Novell NetWare®, and IBM OS/2 Intelligent Server Management |
| OS Support |
| Tru64 UNIX systems include pre-installed software, base license, unlimited user license, server extension license, and Open Source Internet Solutions. OpenVMS systems include pre-installed software, base license, and Enterprise Integration Server License Package V3.0A. |
| Service and Support |
| Protected by Compaq Services, including a three-year, on-site hardware warranty with next business day response. Software warranty is a 90-day telephone advisory. Training, consulting, network integration, software support, comprehensive system maintenance and guaranteed uptime services are also available for customers requiring higher levels of service and support. |

| System requirements: |
| --- |
| Tru64 UNIX V4.0F or OpenVMS V7. 2-1 |
| Mandatory selection of IDE or SCSI system disk drive |
| SCSI adapter and SCSI cable kit required for internal SCSI disks and tape |
| Country-specific keyboard and power cord for all non-North American orders |
| Software media and documentation for first system on site |
| Note: For system integration of any options with 6-3 part numbers, contact CustomSystems. |
| Mandatory Options |
| Maximum three internal disk drives |
| Systems support 3.5( x 1( internal drives only |
| IDE Disk Drive |
| 10-GB 5400 rpm IDE drive | 3X-RE56A-AA |
| SCSI Disk Drives |
| 9.1-GB 7,200 rpm UltraSCSI drive | DS-RZ2DA-WA |
| 9.1-GB 10,000 rpm UltraSCSI drive | DS-RZ1DD-WA |
| 18-GB 7,200 rpm UltraSCSI drive | DS-RZ2EA-WA |
| SCSI Adapters |
| PCI 1-port UltraSCSI single-ended adapter | KZPBA-CA |
| PCI 2-port UltraSCSI single-ended adapter and 10/100 Mbit Ethernet combo adapter | KZPCM-DA |
| PCI 1-channel Wide Ultra-2 (LVD) SCSI adapter | SN-KZPCA-AA |
| PCI 1-port UltraSCSI RAID controller | KZPAC-AA |
| PCI 3-port UltraSCSI RAID controller | KZPAC-CA/CB |
| SCSI Cable Kit |
| SCSI cable kit (includes SCSI cable and SCSI LED cable) | 3X-BN50A-03 |
| Memory |
| Maximum 2-GB memory |
| Systems include one memory kit; maximum 2 memory kits per system(Each kit includes two industry-standard DIMMs with ECC support |
| 128-MB memory kit, two 200-pin, 100 MHz, 64-MB DIMMs | 3X-MS310-BA |
| 256-MB memory kit, two 200-pin, 100 MHz, 128-MB DIMMs | 3X-MS310-CA |
| 512-MB memory kit, two 200-pin, 100 MHz, 256-MB DIMMs | 3X-MS310-DA |
| 1 GB memory kit, two 200-pin, 100 MHz, 512-MB DIMMs | 3X-MS310-EA |

| Internal Storage |
| --- |
| Systems include 600-MB 32X CD-ROM drive and 1.44-MB diskette drive in dedicated drive slots. |
| Additional internal storage supported: Three 1( hard disk drive bays One removable 5.25( half-height removable media bay; note that one 3.5( x 1( hard disk drive is supported in removable media bay |
| SCSI adapter and SCSI cable kit required for SCSI disks or tapes |
| See “Mandatory Options” for supported disk drives and SCSI cable kit |
| Removable Media Devices |
| TLZ10 DAT 4 mm Internal tape drive (requires SN-PBXKP-BA wide-to-narrow SCSI adapter) | TLZ10-LB |
| Wide-to-narrow SCSI adapter | SN-PBXKP-BA |
| External Storage |
| Tabletop DAT Tape Drives |
| 4 mm DAT SCSI (SDT 9000) tabletop drive | DS-TLZ10-DB |
| 20/40-GB SCSI (DLT 4000E) tabletop drive | TZ88N-TA |
| 32/64-GB tabletop DAT loader | TLZ9L-DB |
| 5, 7, 10, 14-GB 8 mm tabletop, single-ended SCSI | TKZ9F-TA |
| 32/64-GB DAT loader in carrier | TLZ9L-VA |
| Hard Disk Drives Supported in StorageWorks Shelf |
| 9.1-GB 7,200 rpm UltraSCSI disk drive | DS-RZ1DA-VW |
| 18.2-GB 7,200 rpm UltraSCSI disk drive | DS-RZ1EA-VW |
| 36.4-GB 7,200 rpm UltraSCSI disk drive | DS-RZ1FB-VW |
| 9.1-GB 10,000 rpm UltraSCSI disk drive | DS-RZ1DD-VW |
| 18.2-GB 10,000 rpm UltraSCSI disk drive | DS-RZ1ED-VW |
| Controllers/Adapters |
| PCI 1-port UltraSCSI Single-ended adapter (uses one PCI slot); includes internal 68-pin and 50-pin HD connectors and external 68-pin HD connector( maximum two per system | KZPBA-CA |
| PCI 1-port UltraSCSI Differential adapter (uses one PCI slot); includes external 68-pin HD connector( maximum two per system | KZPBA-CB |
| PCI 2-port UltraSCSI Single-ended adapter and 10/100 Mb Ethernet combo adapter (uses 1PCI slot) ( maximum two per system | KZPCM-DA |
| External Storage (continued) |
| Controllers/Adapters (continued) |
| 68-pin HD male-to-VHDCI male UltraSCSI cable; required for each external UltraSCSI shelf attached to KZPBA-CA/CB adapter | BN38C-xx |
| PCI 1-port UltraSCSI RAID controller with 4-MB cache memory, includes RAID Array 230/Plus Subsystem software and documentation kit and VHDCI female connector; tape drives not supported, maximum two per system(18.2-GB or higher disk drives not supported on KZPAC-xx RAID controllers | KZPAC-AA |
| PCI 3-port UltraSCSI RAID controller with 4-MB cache memory, includes RAID Array 230/Plus Subsystem Software and documentation kit; tape drives not supported; SCSI cable required for each active port; requires BN31K-0E for external third-port connection, maximum two per system(18.2-GB or higher disk drives not supported on KZPAC-xx RAID controllers | KZPAC-CA |
| Same as KZPAC-CA with 8-MB cache memory | KZPAC-CB |
| Cache battery backup for KZPAC controller | KZPSC-UB |
| SCSI cable/bulkhead assembly kit with KZPAC-CA/CB, allows external connection of one third port | BN31K-0E |
| SCSI cable/bulkhead assembly kit with two ports for KZPAC-CA/CB, allows external connection of two third ports | KZPAC-SB |
| Graphics Option |
| ELSA Gloria Synergy graphics with 8-MB SGRAM 1024 x 768, 2D/3D graphics accelerator; Tru64 UNIX V4.0F( 2-head support, OpenVMS V7.2-1( 3-head support | SN-PBXGK-BB |
| PowerStorm 350 graphics( maximum three per Tru64 UNIX systems only | SN-PBXGD-AE |

| Monitors |
| --- |
| Graphics monitors other than those listed below can be used if compatible with SVGA graphics ordered with system. |
| Selection of video extension cable and country-specific power cord is mandatory for all monitors. |
| 15( Corporate Series auto-scan color monitor, VGA to 1024 x 768 @ 85 Hz; Northern Hemisphere without power cord | 3R-VRQV5-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQV5-11 |
| 17( (16( viewable image size) professional series auto-scanning color monitor, Trinitron CRT, 0.25 mm aperture grill pitch, VGA to 1280 x 1024 at 75 Hz, TCO 95, MPR-II, Energy Star, attached 1.8-m video cable; Northern Hemisphere without power cord | 3R-VRQP7-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQP7-23 |
| 21( (19.6( viewable image size) auto-scanning color monitor, Trinitron CRT, 0.25 mm aperture grill pitch, VGA to 1600 x 1200 at 75 Hz NI, TCO 95, Energy Star, includes 1.8-m video cable; Northern Hemisphere without power cord | 3R-VRQP1-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQP1-23 |
| Video Extension Cable |
| 1.8-m video extension cable; order one for each monitor | BN39C-02 |
| Monitor Power Cords |
| North America | BN26J-1K |
| Japan, 2.5 m, Dentori approved | 3X-BN46F-02 |
| Australia, New Zealand, 2.5 m | BN19H-2E |
| Central Europe, 2.5 m | BN19C-2E |
| UK, Ireland, 2.5 m | BN19A-2E |
| Switzerland, 2.5 m | BN19E-2E |
| Denmark, 2.5 m | BN19K-2E |
| Italy, 2.5 m | BN19M-2E |
| Egypt, India, South Africa, 2.5 m | BN19S-2E |
| Israel, 2.5 m | BN18L-2E |
| Keyboards |
| Systems ordered in North America include U.S./English keyboard; selection of a country specific keyboard is mandatory for all non-North American orders |
| Tru64 UNIX U.S./English keyboard | SN-LKQ47-AA |
| Tru64 UNIX Belgian keyboard | SN-LKQ47-AB |
| Tru64 UNIX Canadian/French keyboard | SN-LKQ47-AC |
| Tru64 UNIX Danish keyboard | SN-LKQ47-AD |
| Tru64 UNIX UK keyboard | SN-LKQ47-AE |
| Tru64 UNIX Finnish keyboard | SN-LKQ47-AF |
| Tru64 UNIX German keyboard | SN-LKQ47-AG |
| Tru64 UNIX Dutch keyboard | SN-LKQ47-AH |
| Tru64 UNIX Italian keyboard | SN-LKQ47-AI |
| Tru64 UNIX Swiss/French keyboard | SN-LKQ47-AK |
| Tru64 UNIX Swedish keyboard | SN-LKQ47-AM |
| Tru64 UNIX Norwegian keyboard | SN-LKQ47-AN |
| Tru64 UNIX French keyboard | SN-LKQ47-AP |
| Tru64 UNIX Latin-American keyboard | SN-LKQ47-AR |
| Tru64 UNIX Spanish keyboard | SN-LKQ47-AS |
| Tru64 UNIX Hebrew keyboard | SN-LKQ47-AT |
| Tru64 UNIX Portuguese keyboard | SN-LKQ47-AV |
| Tru64 UNIX BHCSY keyboard | SN-LKQ47-AX |
| Tru64 UNIX International keyboard | SN-LKQ47-BA |
| Tru64 UNIX Greek keyboard | SN-LKQ47-BH |
| Tru64 UNIX Taiwanese keyboard | SN-LKQ47-BI |
| Tru64 UNIX Korean keyboard | SN-LKQ47-BK |
| Tru64 UNIX Polish keyboard | SN-LKQ47-BP |
| Tru64 UNIX Hungarian keyboard | SN-LKQ47-BQ |
| Tru64 UNIX Arabic keyboard | SN-LKQ47-BR |
| Tru64 UNIX Cyrillic keyboard | SN-LKQ47-BT |
| Tru64 UNIX Turkish keyboard | SN-LKQ47-BU |
| Tru64 UNIX Czech keyboard | SN-LKQ47-BV |
| Tru64 UNIX Thai keyboard | SN-LKQ47-CB |
| Tru64 UNIX S. Chinese keyboard | SN-LKQ47-CV |
| Tru64 UNIX Slovak keyboard | SN-LKQ47-CZ |
| OpenVMS U.S./English keyboard | LK461-A2 |
| OpenVMS Belgian keyboard | LK461-AB |
| OpenVMS Canadian/French keyboard | LK461-AC |
| OpenVMS Danish keyboard | LK461-AD |
| OpenVMS Finnish keyboard | LK461-AF |
| OpenVMS German keyboard | LK461-AG |
| OpenVMS Dutch keyboard | LK461-AH |
| OpenVMS Italian keyboard | LK461-AI |
| OpenVMS Swiss/French keyboard | LK461-AK |
| OpenVMS Swiss/German keyboard | LK461-AL |
| OpenVMS Swedish keyboard | LK461-AM |
| OpenVMS Norwegian keyboard | LK461-AN |
| Keyboards (continued) |
| OpenVMS French keyboard | LK461-AP |
| OpenVMS Canadian/English keyboard | LK461-AQ |
| OpenVMS Spanish keyboard | LK461-AS |
| OpenVMS Hebrew keyboard | LK461-AT |
| OpenVMS Portuguese keyboard | LK461-AV |
| OpenVMS Greek keyboard | LK461-BH |
| OpenVMS Romanian keyboard | LK461-BL |
| OpenVMS Polish keyboard | LK461-BP |
| OpenVMS Hungarian keyboard | LK461-BQ |
| OpenVMS Cyrillic keyboard | LK461-BT |
| OpenVMS Turkish keyboard | LK461-BU |
| OpenVMS Czech keyboard | LK461-BV |
| OpenVMS Turkish-French keyboard | LK461-BW |
| OpenVMS Yugoslavian keyboard | LK461-BY |
| OpenVMS Slovak keyboard | LK461-CZ |
| Power Cords |
| Pedestal |
| Systems ordered in North America include BN26J-1K 120V North American power cord; selection of country-specific power cord is mandatory for all non- North American orders. |
| North America, 2.5 m | 3X-BN46K-2E |
| Japan, 2.5 m, Dentori approved | 3X-BN46G-02 |
| Australia, New Zealand, 2.5 m | BN19H-2E |
| Central Europe, 2.5 m | BN19C-2E |
| UK, Ireland, 2.5 m | BN19A-2E |
| Switzerland, 2.5 m | BN19E-2E |
| Denmark, 2.5 m | BN19K-2E |
| Italy, 2.5 m | BN19M-2E |
| Egypt, India, South Africa, 2.5 m | BN19S-2E |
| Israel, 2.5 m | BN18L-2E |
| Rackmount |
| North America, 4.5 m | BN20Z-4E |
| Non-North America, 4.5 m | 3X-BN46L-4E |
| Japan, Dentori approved, 4.5 m | 3X-BN46D-4E |
| M-Series Cabinet Enclosures and Accessories |
| M-Series Rackmount Kit |
| Rackmount kit must be ordered separately. |
| DS10 M-Series rackmount kit | 3X-PBX01-AB |
| M-Series Cabinet Enclosure |
| Cabinet enclosures, top gun blue, are available in three sizes: 43( cabinet enclosure (H9A11-xx) 20U or 35( of usable vertical space 67( cabinet enclosure (H9A10-xx) 31U or 54.2( of usable vertical space 79( cabinet enclosure (H9A15-xx) 38U or 66.5" of usable vertical space |

# M-Series Cabinet Configuration Chart for AlphaServer DS10

| Cabinet | Mounting Kit | Cabinet Height / Space | System | Shelves | Ballast Kit |
| --- | --- | --- | --- | --- | --- |
| H9A11-MC/MD | Optional, must be ordered separately 3X-PBX01-AB | 35( / 20U | 1 2 3 4 or 5 6 | 6 6 4 2 0 | 1 1 0 0 0 |
| H9A10-MC/MD | Optional, must be ordered separately 3X-PBX01-AB | 54.2( / 33U | 1 2 3, or 4 5 6 7 8, 9, or 10 | 6 6 6 6 4 2 0 | 2 2 1 1 0 0 0 |
| H9A15-MC/MD | Optional, must be ordered separately 3X-PBX01-AB | 66.5( / 40U | 1 2 3 4, or 5 6 7 or 8 9 or 10 11 or 12 | N/A 6 6 6 6 4 2 0 | N/A 2 2 1 0 0 0 0 |

| M-Series Cabinet Enclosures and Accessories (continued) |
| --- |
| M-series Cabinet Enclosure Options |
| M-series Cabinet Enclosures require the mandatory selection of the following items: |
| H9A11, H9A10, or H9A15 Cabinet, 120V or 240V |
| Cabinet front door based on cabinet height (optional on H9A11 cabinet) |
| Factory Integration |
| Ballast kits as required |
| Cabinet Enclosures |
| 120V 24A controller with 10 NEMA 5-15R outlets, input power plug NEMA L5-30P, Americas, Asia Pacific; includes rear door, H7600-AA power distribution unit, trim kit, and front filler bezel kit | H9A11-MC |
| 240V 16A controller with 12 IEC C13 outlets, input power plug IEC 309, 16A, Europe; includes rear door, H7600-DB power distribution unit, trim kit, and front filler bezel kit | H9A11-MD |
| 120V dual-24A controller, each with 10 NEMA 5-15R outlets, input power plug NEMA L5-30P, Americas, Asia Pacific; includes rear door, top fan tray, and two H7600-AA power distribution units | H9A10-MC |
| 240V dual-16 A controller, each with 12 IEC C13 outlets, input power plug IEC 309, 16A, Europe; includes rear door, top fan tray, and 2 H7600-DB power distribution units | H9A10-MD |
| 120V dual-24A controller, each with 10 NEMA 5-15R outlets, input power plug NEMA L5-30P, Americas, Asia Pacific; includes rear door, top fan tray, and two H7600-AA power distribution units | H9A15-MC |
| 240V dual-16A controller, each with 12 IEC C13 outlets, input power plug IEC 309, 16A, Europe; includes rear door, top fan tray, and two H7600-DB power distribution units | H9A15-MD |
| Cabinet Front Door |
| Top gun blue front door for H9A10-MC/MD Cabinet Enclosure | H9C10-TF |
| Top gun blue front door for H9A15-MC/MD Cabinet Enclosure | H9C15-TF |
| Top gun blue front door for H9A11-MC/MD Cabinet Enclosure: selection of front door for H9A11 is optional, cabinet includes front trim kit and filler bezel | H9C11-EB |
| Shelves supported in M-series Cabinets with front doors (H9A10/M9A15) |
| StorageWorks UltraSCSI single bus, single-ended shelf with 180 W power supply and RETMA mounting kit | BA36R-RC |
| M-Series Cabinet Enclosures and Accessories (continued) |
| Shelves supported in M-series Cabinets with front doors (H9A10/M9A15) (continued) |
| StorageWorks UltraSCSI split bus, single-ended shelf with 180 W power supply and RETMA mounting kit | BA36R-RD |
| StorageWorks controller shelf with RETMA mounting kit and NEMA power for H9A10-MC, H9A15-MC cabinets (Americas, Asia Pacific); order BN30B-02 power cord for H9A10-MD, H9A15-MD cabinets (Europe) | BA35R-MR |
| 180W power supply | CK-BA35X-HH |
| Shelves supported in M-series Cabinets with trim kit (H9A11) |
| StorageWorks UltraSCSI single bus, single-ended shelf with 180 W power supply and RETMA mounting kit, blue bezel | BA35C-AA |
| StorageWorks UltraSCSI split bus, single-ended shelf with 180 W power supply and RETMA mounting kit, blue bezel | BA35C-BA |
| BA370 Rackmounted Enclosure/Rear Cabinet Extender |
| BA370 front-mount rackmount enclosure includes RETMA rackmount kit; first BA370 enclosure must be front mounted in cabinet, 20U height | 2T-BA370-AS |
| BA370 rear-mount rackmount enclosure includes RETMA rackmount kit; second BA370 enclosure must be rear mounted in cabinet, 20U height Note that Rear Cabinet Extender, H9C10-TE or H9C15-TE, is mandatory for second BA370 | 2T-BA370-AR |
| Rear cabinet extender, top gun blue, for H9A10-MC/MD cabinets | H9C10-TE |
| Rear cabinet extender, top gun blue, for H9A15-MC/MD cabinets | H9C15-TE |
| Factory Integration |
| Factory Integration of systems and storage devices assembled and configured in cabinet enclosure for H9A10/15 cabinet enclosures | YS-ASCAA-AA |
| Factory Integration of systems and storage devices assembled and configured in cabinet enclosure for H9A11 cabinet enclosures | YS-ASCAA-AB |
| M-Series Cabinet Enclosures and Accessories (continued) |
| Ballast Kit |
| Ballast is dead weight added to a cabinet at specific locations for specific configurations to meet safety regulations for installation, operation, and service; see Cabinet Configuration Chart for ballast kit requirements |
| Two 35-40 lb steel plates | H9C10-MC |
| For more information on M-series Cabinet Enclosures: www.digital.com/alphaserver/products/m-series.html |
| Rackmount System Management Station for M-series Cabinets |
| M-Series cabinets accommodate Rackmount System Management Station components. For configuration and ordering information for console switches, flat panel display, and rackmounted keyboard drawer refer to: http://www.compaq.com/products/options/index-rack.html |
| Rackmount System Management Station is currently installed onsite only (not factory installed.) Contact CustomSystems for integration of Rackmount System Management Station components into M-Series cabinets. |
| For each Rackmount System Management Station component (control switch, flat panel display, keyboard drawer), order one rear cabinet extension bracket (2T-QH915-03) |
| Compaq CustomSystems Support |
| Cabinets containing systems and storage must be assembled by qualified assemblers: Compaq Manufacturing, Compaq CustomSystems Group, or an authorized Compaq Certified Integration Partner. |
| For custom integration of systems, options, and additional Compaq and third-party devices, or for other cabinets, doors, and trim kits of a different color, contact Compaq CustomSystems at 1-800-AT-COMPAQ (1-800-282-6672), or contact your local authorized Compaq Certified Integration Partner. |
| Network Options |
| Systems include dual embedded 10/100 BaseT Ethernet ports (BN25G-xx cable must be ordered separately) |
| Additional Ethernet ports can be added using available PCI slots |
| PCI 10/100-Mb 1-port Fast Ethernet controller (Twisted Pair); maximum two per system | DE500-BA |
| Network Options (continued) |
| PCI 10/100-Mb 4-Port Fast Ethernet controller (Twisted Pair); maximum two per system | DE504-BA |
| Cable for 10BaseT Twisted Pair connection | BN25G-xx |
| PCI 10/100-Mb Fast Ethernet controller (MMF) | DE500-FA |
| PCI 1-port 10/100-Mb Ethernet adapter (Twisted Pair): maximum two per Tru64 UNIX systems | 3X-DE600-AA |
| PCI 2-port 10/100-Mb Ethernet adapter (Twisted Pair): maximum one per Tru64 UNIX systems | 3X-DE602-AA |
| SC-SC Dual fibre optic cable, mm, pp xx = length in meters | BN34B-xx |
| PCI-to-GbE SX adapter; maximum two per system | DEGPA-SA |
| PCI 4-port asynchronous controller with cable; maximum two PBXDA-xx per system | PBXDA-AA |
| PCI 8-port asynchronous controller with cable; maximum two PBXDA-xx per system | PBXDA-AB |
| PCI 16-port asynchronous controller with cable; maximum two PBXDA-xx per system | PBXDA-AC |
| Software |
| Media and documentation required for first system on site. |
| Software processor code = E |
| Tru64 UNIX |
| Tru64 UNIX systems include Tru64 UNIX Unlimited User license, Server Extension license, Open Source Internet Solutions |
| Tru64 UNIX Media & Documentation kit | QA-MT4AA-H8 |
| Tru64 UNIX Full Documentation kit | QA-MT4AA-GZ |
| TruCluster Available Server License | QL-05SAE-AA |
| Layered products media and documentation for Tru64 UNIX on CD-ROM | QA-054AA-H8 |
| DECnet/OSI end-system license for Tru64 UNIX | QL-MTJAE-AA |
| DECnet/OSI extended function license for Tru64 UNIX | QL-MTKAE-AA |
| Open3D for Tru64 UNIX on CD-ROM, includes graphics drivers | QA-0AFAA-H8 |
| OpenVMS |
| OpenVMS systems include OpenVMS base license with system manager license and Compaq Enterprise Integration Server License Package for OpenVMS Revision V3.0A. |
| Software (continued) |
| OpenVMS (continued) |
| Compaq Enterprise Integration Package includes licenses for TCP/IP Services for OpenVMS, DECwindows Motif for OpenVMS Alpha, DECprint Supervisor for OpenVMS Alpha Plus, DECprint Supervisor for OpenVMS Open, DECnet-Plus for OpenVMS Alpha End System, Archive/Backup System for OpenVMS Management Tools, Archive/Backup Agent for Windows NT, OpenVMS Disk Services for Windows NT, Office Server for OpenVMS, PATHWORKS 32, PATHWORKS V6 for OpenVMS – Advanced Server, and DIGITAL Office Server Client Access License |
| OpenVMS V7.1-2 media and online documentation on CD-ROM | QA-MT1AR-H8 |
| OpenVMS V7.2-1 media and online documentation on CD-ROM | QA-MT1AT-H8 |
| OpenVMS media and online documentation on CD-ROM | QA-MT1AA-H8 |
| OpenVMS hard copy documentation | QA-001AA-GZ |
| Layered products media and documentation for OpenVMS on CD-ROM | QA-03XAA-H8 |
| Open3D for OpenVMS on CD-ROM, includes graphics drivers | QA-0ADAA-H8 |
| Concurrent Use 1-user license | QL-MT3AA-3B |
| Concurrent Use 2-user license | QL-MT3AA-3C |
| Concurrent Use 4-user license | QL-MT3AA-3D |
| Concurrent Use 8-user license | QL-MT3AA-3E |
| Concurrent Use 16-user license | QL-MT3AA-3F |
| Concurrent Use 32-user license | QL-MT3AA-3G |
| Concurrent Use 64-user license | QL-MT3AA-3H |
| Concurrent Use 128-user license | QL-MT3AA-3J |
| Concurrent Use 256-user license | QL-MT3AA-3K |
| Traditional Unlimited User license | QL-MT2AE-AA |
| Hardware and Software Supplemental Services |
| Hardware Supplemental Services |
| Systems include three-year, onsite hardware warranty with next business day response. |
| Select optional Hardware Supplemental Services if required |
| 3-year, 5 x 9, 4-hour response time | FM-MK4HR-36 |
| 5-year, 5 x 9, 4-hour response time | FM-MK4HR-60 |
| 3-year, 5 x 12, 4-hour response time | FM-MK512-36 |
| 5-year, 5 x 12, 4-hour response time | FM-MK512-60 |
| 3-year, 6 x 16, 4-hour response time | FM-MK616-36 |
| 5-year, 6 x 16, 4-hour response time | FM-MK616-60 |
| 3-year, 7 x 24, 4-hour response time | FM-MK724-36 |
| 5-year, 7 x 24, 4-hour response time | FM-MK724-60 |
| Years 4-5, 5 x 9, next day response time | FM-MKXHW-60 |
| Hardware and Software Supplemental Services (continued) |
| Software Supplemental Services |
| 1-year, 5 x 9 Bronze Software Supplemental Support, Tru64 UNIX | FM-D10U9-12 |
| 3-year, 5 x 9 Bronze Software Supplemental Support, Tru64 UNIX | FM-D10U9-36 |
| 5-year, 5 x 9 Bronze Software Supplemental Support, Tru54 UNIX | FM-D10U9-60 |
| 1-year, 7 x 24 Bronze Software Supplemental Support, Tru64 UNIX | FM-D10US-12 |
| 3-year, 7 x 24 Bronze Software Supplemental Support, Tru64 UNIX | FM-D10US-36 |
| 5-year, 7 x 24 Bronze Software Supplemental Support, Tru64 UNIX | FM-D10US-60 |
| 1-year, Bronze Node Software Supplemental Support, Tru64 UNIX | FM-D10UN-12 |
| 3-year, Bronze Node Software Supplemental Support, Tru64 UNIX | FM-D10UN-36 |
| 5-year, Bronze Node Software Supplemental Support, Tru64 UNIX | FM-D10UN-60 |
| 1-year, 5 x 9Bronze Software Supplemental Support, OpenVMS | FM-D10V9-12 |
| 3-year, 5 x 9Bronze Software Supplemental Support, OpenVMS | FM-D10V9-36 |
| 5-year, 5 x 9Bronze Software Supplemental Support, OpenVMS | FM-D10V9-60 |
| 1-year, 7 x 24 Bronze Software Supplemental Support, OpenVMS | FM-D10VS-12 |
| 3-year, 7 x 24 Bronze Software Supplemental Support, OpenVMS | FM-D10VS-36 |
| 5-year, 7 x 24 Bronze Software Supplemental Support, OpenVMS | FM-D10VS-60 |
| 1-year, Bronze Node Software Supplemental Support, OpenVMS | FM-D10VN-12 |
| 3-year, Bronze Node Software Supplemental Support, OpenVMS | FM-D10VN-36 |
| 5-year, Bronze Node Software Supplemental Support, OpenVMS | FM-D10VN-60 |

| System Unit |  | Physical Characteristics |  |
| --- | --- | --- | --- |
|  |  | Dimensions (HxWxD) Weight (maximum) | 5.1 x 17.6 x 19 in/13 x 45 x 48 cm 36 lbs/16.3 kg |
|  |  | Environmental | Operating | Non-Operating |
|  |  | Temperature1 Humidity (non-condensing) Altitude (unpressurized) | 50( to 104(F/10( to 40(C 20% to 80% 10,000 ft / 3,048 m2 | –40( to 151(F/–40( to 66(C 10% to 95% 40,000 ft/12,192 m |
|  |  | Power Requirements |  |
|  |  | Nominal voltage range | 100 to 120 Vac/220 Vac |
|  |  | Operating voltage range | 90 to 128 Vac/180 to 265 Vac |
|  |  | Power source phase | Single/Single |
|  |  | Nominal frequency | 60 Hz/50 Hz |
|  |  | Frequency range | 59 to 61 Hz/49-51 Hz |
|  |  | Maximum inrush current | 11 amps/22 amps |
|  |  | Single power supply (single cordset) | 12 amps/5 amps 7.4 amps each supply/3.7 amps each supply |

Maximum operating temperature at sea level. Reduce by 1.8(F (1(C) for each 2,000 ft (660 m) above sea level.

Higher altitudes are possible if maximum operating temperature is reduced.

# Text boxes

At A Glance

AlphaServer DS10 systems are ideal for ISP/Internet applications, High Performance Technical Computing, software development, and replicated site applications

Alpha processor module with 21264 466-MHz CPU with 2-MB onboard ECC cache

Onboard IDE controller for internal storage

Onboard dual 10/100 BaseT Ethernet ports

Four PCI expansion slots, three 64-bit PCI slots, one 32-bit PCI slot

2-GB maximum memory capacity

1.44-MB diskette drive

600-MB CD-ROM drive

5.25( x 1.6( removable media bay or 3.5( x 1( hard disk drive bay, two 3.5( x 1( hard disk drive bays

Two serial ports, one serial port with full-duplex asynchronous modem control, one RMC dedicated serial port with full- duplex asynchronous modem control

Bi-directional enhanced parallel port

PS/2-style keyboard port and mouse port

300W (120/240V, 60/50 Hz) power supply

3-button mouse

U.S./English keyboard with North American orders

U.S.  power cord with North American orders

U.S. English documentation

Optional rackmount kit must be ordered separately

Tru64( UNIX or OpenVMS Factory Installed Software

90-day software product warranty

Protected by Compaq Services, including three-year, on-site hardware with next business day response

Diskette drive

Fan

PCI riser card

Memory boards

Dual Ethernet ports

Keyboard and mouse ports

CPU and fan

Power supply

Disks

CD-ROM drive

Models

DS10 Tru64 UNIX  Servers
466 MHz CPU

DA-PB10A-AB
(128-MB memory)

DA-PB10A-AC
(256-MB memory)

DA-PB10A-AD
(512-MB memory)

DA-PB10A-AE
(1-GB memory)

DS10 OpenVMS Servers

466 MHz CPU

DY-PB10A-AB
(128-MB memory)

DY-PB10A-AC
(256-MB memory)

DY-PB10A-AD
(512-MB memory)

DY-PB10A-AE
(1-GB memory)