| Processor |
| --- |
| Alpha 21264 processor 466 MHz |
| Cache Memory |
| 2-MB onboard cache |
| Upgradability |
| Supports upgrades of memory and hard drives |
| Standard | One CPU |
| Memory (Two DIMM Slots) |
| Standard | 128 MB, 256 MB, 512 MB, or 1 GB (one memory kit) |
| Maximum | 1 GB (One memory kit) |
| Network Controller |
| Onboard dual 10/100 BaseT Ethernet ports |
| Expansion |
| PCI slots | One full length slot |
| Storage Controller |
| Onboard IDE controller for internal storage, PCI SCSI controller optional |
| Storage |
| Diskette Drive/CD-ROM | Optional |
| Hard Drives | 10-GB IDE disk drive or 9.1-GB and 18.2-GB UltraSCSI disk drives available |
| Expansion Ports |
| Parallel | One bi-directional enhanced port |
| Serial | One serial port: Selectable as either one full duplex asynchronous modem control serial port or one RMC dedicated asynchronous modem control serial port |
| Pointing Device (Mouse) | One port |
| Keyboard | One PS/2-style port |
| USB | Two (future support) |
| Form Factor |
| 1 U Rackmount or Desktop (1.75” h x 17.5” w x 20.5” d), 20 lbs. |
| Manageability |
| Compaq Insight Manager |
| Power Supply |
| 150-Watt Power Supply |
| OS Support |
| AlphaServer Tru64 UNIX systems include pre-installed software, base license, unlimited user license, server extension license, Open Source Internet Solutions, and Netscape Enterprise Server 3.0 AlphaServer OpenVMS systems include pre-installed software, base license, TCP/IP Services for OpenVMS, DECWindows Motif for OpenVMS Alpha, DECnet Plus for OpenVMS End System, and Pathworks 32 Linux-Ready systems ship without system software. Red Hat 6.0 or SuSe 6.1 Linux may be purchased separately from a Linux distributor. Minimum Compaq OS support: Tru64 UNIX V4.0F, OpenVMS V7.1-2 or V.2-1. |
| Service and Support |
| Compaq Services provides a wide range of service offerings including a one-year limited warranty fully supported by a worldwide network of resellers and service providers; lifetime toll-free 7 x 24 hardware technical phone support. |

| Step 1 ( Select system |
| --- |
| AlphaServer DS10L systems require the mandatory selection of the following items: System disk drive - If SCSI disk is selected, adapter and cable kit are required - If IDE disk is selected, cable kit is required Power cord if used as desktop system Rackmount systems require rackmount kit and cable management kit Software media and documentation for first system onsite Notes: AlphaServer DS10L systems do not include keyboard, mouse, power cords, rackmount kits, CD-ROM, or floppy drives; order as required. Rackmount system minimum for factory integration is four AlphaServer DS10L minimum OS support ( Tru64 UNIX V4.0F, OpenVMS V7.2-1 For system integration of options with 6-3 part numbers, contact CustomSystems (1-800-AT-COMPAQ) |
| OS | CPU | Memory | Order No. |
| Tru64 UNIX | 466 MHz | 128 MB | DA-71AAA-CA |
| Tru64 UNIX | 466 MHz | 256 MB | DA-71AAA-DA |
| Tru64 UNIX | 466 MHz | 512 MB | DA-71AAA-EA |
| Tru64 UNIX | 466 MHz | 1 GB | DA-71AAA-FA |
| OpenVMS | 466 MHz | 128 MB | DY-71AAA-CA |
| OpenVMS | 466 MHz | 256 MB | DY-71AAA-DA |
| OpenVMS | 466 MHz | 512 MB | DY-71AAA-EA |
| OpenVMS | 466 MHz | 1 GB | DY-71AAA-FA |
| Linux-Ready | 466 MHz | 128 MB | DJ-71AAA-CA |
| Linux-Ready | 466 MHz | 256 MB | DJ-71AAA-DA |
| Linux-Ready | 466 MHz | 512 MB | DJ-71AAA-EA |
| Linux-Ready | 466 MHz | 1 GB | DJ-71AAA-FA |
| Step 2 ( Select mandatory options |
| Step 2a ( System Disk Drive ( Mandatory |
| Maximum two internal disk drives. The second drive is installed in the media bay. Select either a CD-ROM/floppy drive or second internal disk – not both – or leave the media bay empty. |
| Internal support for 3.5( x 1( drives only |
| For multiple system configurations that share a system disk external to system enclosure, contact Compaq CustomSystems. |
| IDE Disk Drive |
| 10-GB 5400 rpm IDE drive | 3X-RE56A-AA |
| 30-GB 7200 rpm IDE drive | 3X-RE57A-BA |
| System Disk Cable Configuration Rules |
| 2 IDE hard disks 2 3X-BN50A-04 ( One drop IDE cable |
| 1 IDE hard disk, 1 SCSI hard disk 1 3X-BN50A-05 ( One drop SCSI cable, LED activity cable, and 68-50-pin adapter 1 3X-BN50A-04 ( One drop IDE cable |
| 1 IDE hard disk, Floppy/CD combo 1 3X-PBXRY-AA ( Floppy/CD combo with one drop IDE cable and floppy cable 1 3X-BN50A-04 ( 17-04803-02 one drop IDE cable |

| 1 SCSI hard disk, Floppy/CD combo 1 3X-BN50A-05 ( One drop SCSI cable, ED activity cable, and 68-50-pin adapter 1 3X-PBXRY-AA ( Floppy/CD combo with one drop IDE cable and floppy cable |
| --- |
| 2 SCSI hard disks 1 3X-BN50A-02 ( Two drop SCSI cable, LED activity cable |
| SCSI Disk Drives |
| 9.1-GB 7200 rpm Ultra2 SCSI drive | DS-RZ2DA-WA |
| 9.1-GB 10000 rpm Ultra2 SCSI drive | DS-RZ1DD-WA |
| 18.2-GB 7200 rpm Ultra2 SCSI drive | DS-RZ2EA-WA |
| 18.2-GB 10000 rpm Ultra2 SCSI drive | DS-RZ2EF-WA |
| Step 2b ( SCSI Adapter ( (SCSI disks require SCSI adapter) |
| SCSI adapter and SCSI cable kit required for internal SCSI disks and tape |
| PCI 1-port UltraSCSI single-ended adapter | KZPBA-CA |
| PCI 1-port UltraSCSI differential adapter | KZPBA-CB |
| PCI 2-port UltraSCSI single-ended adapter and 10/100 Mbit Ethernet combo adapter (Tru64 UNIX and OpenVMS only) | KZPCM-DA |
| PCI 1-channel Wide Ultra-2 (LVD) SCSI adapter | SN-KZPCA-AA |
| PCI 1-port UltraSCSI RAID controller (Tru64 UNIX and OpenVMS only) | KZPAC-AA |
| SCSI Cable Kit (Refer to “System Disk Cable Configuration Rules”) |
| Step 2c ( Power Cords -- Mandatory for desktop systems |
| For rackmount systems refer to Step 5, PDU/Fan/Cable Management Kits |
| Desktop Power Cords |
| North American 120V, 75( | BN26J-1K |
| Australia, New Zealand, 2.5m | BN19H-2E |
| Central Europe, 2.5m | BN19C-2E |
| UK, Ireland, 2.5m | BN19A-2E |
| Switzerland, 2.5m | BN19E-2E |
| Denmark, 2.5m | BN19K-2E |
| Italy, 2.5m | BN19M-2E |
| Egypt, India, South Africa, 2.5m | BN19S-2E |
| Israel, 2.5m | BN18L-2E |
| Japan, 2.5m | 3X-BN46F-02 |
| Step 3 ( Memory ( Optional |
| Maximum 1-GB memory |
| Systems include one memory kit; maximum one memory kit per system ( each kit includes two industry-standard DIMMs with ECC support |
| To increase memory, order new memory and replace resident memory with the new DIMMS |
| 128-MB memory kit, two 200-pin, 100 MHz, 64-MB DIMMs | 3X-MS310-BA |
| 256-MB memory kit, two 200-pin, 100 MHz, 128-MB DIMMs | 3X-MS310-CA |
| 512-MB memory kit, two 200-pin, 100 MHz, 256-MB DIMMs | 3X-MS310-DA |
| 1-GB memory kit, two 200-pin, 100 MHz, 512-MB DIMMs | 3X-MS310-EA |

| Step 4 ( Internal Storage ( Optional |
| --- |
| System includes one bay in system enclosure; optional bay may be used as a media bay or drive bay: - One 1( hard disk drive bay (refer to Step 2a) or - One 3.5( x 1( hard disk drive supported in removable media bay |
| SCSI adapter and SCSI cable kit required for SCSI disks or tapes |
| 1.44-MB diskette drive/600-MB 24X CD-ROM combo | 3X-PBXRY-AA |
| 20/40-GB DAT tape drive, top gun blue | 3X-SD20X-LB |
| 35/70-GB AIT tape drive, top gun blue | 3X-SZ35X-LB |
| 50/100-GB AIT tape drive, top gun blue | 3X-SZ50X-LB |
| Note: Refer to “System Disk Cable Configuration Rules” in Step 2 |
| Step 5 ( M-series Cabinet Enclosures ( Optional |
| M-Series cabinet enclosures support up to 40 DS10L systems and/or up to three StorageWorks shelves. M-series enclosures require selection of the following items: |
| H9A11, H9A10, or H9A15 Cabinet, 120V or 240V |
| Minimum four AlphaServer DS10L systems for rack configuration; minimum five systems for H9A15 cabinet |
| Rack kit for each system (or quad rack for every four systems) |
| PDU/Fan/Cable management kit according to the configuration chart |
| Cabinet front door based on cabinet height (optional for H9A11 cabinet) |
| Factory integration |
| Ballast kit according to the configuration chart |
| Power Cord |
| Up to six BA356 shelves supported; back-to-back mounting not allowed |
| AlphaServer DS10L Rackmount Configuration Rules |
| Minimum number of systems orderable in a rack is four for H9A11 or H9A10 cabinets; minimum of five for H9A15 cabinet |
| Power cords are only available in cable management kits as follows: The first eight systems in an H9A11 cabinet or the first 16 systems in an H9A10 or H9A15cabinet require a fan/cable management kit. For every 1-8 additional systems, a PDU/fan/cable management kit is required. |
| Note: For more information on M-Series Cabinet Enclosures, see www.digital.com/alphaserver/products/m-series/index.html |
| Cabinet | Rack Kits 3X-PBX01-BC quad | Rack kit 3X-PBX01-BB single | Systems 1U | Shelves @ 4U | Fan Kit 3X-H7210-BA/BB/BC | PDU Kit 3X-H7210-AA/AB/AC | Ballast H9C10-MC |
| H9A11, H9A10, H9A15 | 1 for each set of 4 systems | 1 for each additional system | Per rack | Per rack | Used with existing PDU | Used when PDU is required |  |
| H9A11-MC/MD | 1 or 2 | 0 to 3 | 4-8 | 3 | 1 | 0 | 0 |
|  | 2 or 3 | 0 to 3 | 9-12 | 2 | 1 | 1 | 0 |
|  | 3 or 4 | 0 to 3 | 13-16 | 1 | 1 | 1 | 0 |
|  | 4 or 5 | 0 to 3 | 17-20 | 0 | 1 | 2 | 0 |
| H9A10-MD/MC | 1 or 2 | 0 to 3 | 4-8 | 6 | 1 | 0 | 21 |
|  | 2 or 3 | 0 to 3 | 9-12 | 5 | 2 | 0 | 0 |
|  | 3 or 4 | 0 to 3 | 13-16 | 4 | 2 | 0 | 0 |
|  | 4 or 5 | 0 to 3 | 17-20 | 3 | 2 | 1 | 0 |
|  | 5 or 6 | 0 to 3 | 21-24 | 2 | 2 | 1 | 0 |
|  | 6 or 7 | 0 to 3 | 24-28 | 1 | 2 | 2 | 0 |
|  | 7 or 8 | 0 to 3 | 29-32 | 0 | 2 | 2 | 0 |
| H9A15-MC/MD | 1 to 2 | 0 to 3 | 5-8 | 6 | 1 | 0 | 2 |
|  | 2 or 3 | 0 to 3 | 9-12 | 5 | 2 | 0 | 1 |
|  | 3 or 4 | 0 to 3 | 13-16 | 4 | 2 | 0 | 0 |
|  | 4 or 5 | 0 to 3 | 17-20 | 3 | 2 | 1 | 0 |
|  | 5 or 6 | 0 to 3 | 21-24 | 3 | 2 | 1 | 0 |
|  | 6 or 7 | 0 to 3 | 25-28 | 3 | 2 | 2 | 0 |
|  | 7 or 8 | 0 to 3 | 29-32 | 2 | 2 | 2 | 0 |
|  | 8 or 9 | 0 to 3 | 33-36 | 1 | 2 | 3 | 0 |
|  | 9 or 10 | 0 to 3 | 37-40 | 0 | 2 | 3 | 0 |
| With 4, 5, and 6 systems, two ballast kits are required, with 7 and 8 systems, one ballast kit is required |
| Cabinet Configuration Chart for AlphaServer DS10L with StorageWorks RA3000 and Disk Shelves |
| 12U of vertical cabinet space is reserved for one RA3000 controller shelf and up to four disk shelves mounted in top of cabinet, front to back; an additional 2U of vertical space is required for RA3000 controller shelf UPS. |
| RAID Array 3000 and UPS each require a separate PDU (H7600-AA/DB) |
| Disk shelves can be a combination of RA3000 DS-SWXRA-GN disk shelves and StorageWorks BA36R-RC/RD disk shelves. |
| RA3000 controller shelf supports a maximum of four DS-SWXRA-GN disk shelves; third and fourth DS-SWXRA-GN disk shelf ordered will be installed in rear of M-series cabinet; rear mounted shelves require that a 2-m SCSI cable (BN37A-02) be ordered separately. |
| Systems are supported in remaining vertical space. The table below considers space requirements for the RA3000, systems, PDU kits, and UPS. |
| 1.75( or 1U space is required between each system unit. |
| Cabinet | Mounting Kit | Cabinet Height / Space | Systems | RA3000 + Shelves |
| H9A11-MX | 3X-PBX01-BB | 35" / 20U | 4-6 | 1 + 2 |
|  |  |  | 7-8 | 1 + 1 (basic) |
| H9A10-MC/MD | 3X-PBX01-BB | 54.2( / 32U | 4-8 | 1 + 4 (max) |
|  |  |  | 9-14 | 1 + 2 |
|  |  |  | 15-23 | 1 + 1 (basic) |
| H9A15-MC/MD | 3X-PBX01-BB | 66.5( / 40U | 5-16 | 1 + 4 (max) |
|  |  |  | 17-22 | 1 + 3 |
|  |  |  | 23-24 | 1 + 2 |
|  |  |  | 25-30 | 1 + 1 (basic) |
| Cabinet Configuration Chart for AlphaServer DS10Lwith StorageWorks BA370 and Disk Shelves |
| 20U of vertical cabinet space is reserved for one front-mounted BA370 rackmount. Note that top fan (1U) is removed from cabinet when BA370 rackmount enclosure is installed. Additional PDU is required to support the BA370. |
| Systems and StorageWorks shelves are supported in remaining vertical space; StorageWorks shelves are not supported in rear of cabinet behind a front-mounted BA370 rackmount enclosure. |
| 1.75( or 1U space is required between each system unit. |
| Cabinet | Rack Kit | Cabinet Height/Space | Systems | BA370 | Shelves |
| H9A10-MC/MD | 3X-PBX01-BB | 56” / 32U | 13 | 1 (front) | 2 |
| H9A15-MC/MD | 3X-PBX01-BB | 66.5” / 40U | 20 | 1 (front) | 6 |
| Note: Installing one BA370 and one system in H9A15 cabinet requires the mandatory selection of a ballast kit |
| H9A11 Cabinet | H9A10 Cabinet | H9A15 Cabinet |
| M-series Cabinets |
| 43" cabinet enclosure with 35" or 20U of usable vertical space; 120V 24A controller with 10 NEMA 5-15R outlets, input power plug NEMA L5-30P, Americas, Asia Pacific; includes rear door, H7600-AA power distribution unit, trim kit, and front filler bezel kit | H9A11-MC |
| 43" cabinet enclosure with 35" or 20U of usable vertical space; 240V 16A controller with 12 IEC C13 outlets, input power plug IEC 309, 16A, Europe; includes rear door, H7600-DB power distribution unit, trim kit, and front filler bezel kit | H9A11-MD |
| 67" cabinet enclosure with 54.2" or 33U of usable vertical space; 120V dual-24A controller, each with 10 NEMA 5-15R outlets, input power plug NEMA L5-30P, Americas, Asia Pacific; includes rear door, top fan tray, and two H7600-AA power distribution units | H9A10-MC |
| 67" cabinet enclosure with 54.2" or 33U of usable vertical space; 240V dual-16 A controller, each with 12 IEC C13 outlets, input power plug IEC 309, 16A, Europe; includes rear door, top fan tray, and two H7600-DB power distribution units | H9A10-MD |
| 79" cabinet enclosure with 66.5" or 40U of usable vertical space; 120V dual-24A controller, each with 10 NEMA 5-15R outlets, input power plug NEMA L5-30P, Americas, Asia Pacific; includes rear door, top fan tray, and two H7600-AA power distribution units | H9A15-MC |
| 79" cabinet enclosure with 66.5" or 40U of usable vertical space; 240V dual-16A controller, each with 12 IEC C13 outlets, input power plug IEC 309, 16A, Europe; includes rear door, top fan tray, and two H7600-DB power distribution units | H9A15-MD |
| Cabinet Rackmount Kits – Refer to table above |
| Single rack kit for AlphaServer DS10L | 3X-PBX01-BB |
| Quad rack kit for AlphaServer DS10L | 3X-PBX01-BC |
| PDU/Fan/Cable Management Kits |
| Kits include PDU, fans, shelf, and cables to serve eight AlphaServer DS10L systems. |
| Power Distribution Unit/Fan/Cable Management Kit (North America) | 3X-H7210-AA |
| Power Distribution Unit/Fan/Cable Management Kit (Europe) | 3X-H7210-AB |
| Power Distribution Unit/Fan/Cable Management Kit (Japan) | 3X-H7210-AC |
| Fan/Cable Management Kits |
| Kits include fans, shelf, and cables to serve eight AlphaServer DS10L systems; for use with PDU that ships with cabinet |
| Fan/Cable Management Kit (North America) | 3X-H7210-BA |
| Fan/Cable Management Kit (Europe) | 3X-H7210-BB |
| Fan/Cable Management Kit (Japan) | 3X-H7210-BC |
| Shelves supported in M-series Cabinets with front doors (H9A10, H9A15) |
| StorageWorks UltraSCSI single bus, single-ended shelf with 180W power supply and RETMA mounting kit | BA36R-RC |
| StorageWorks UltraSCSI split bus, single-ended shelf with 180W power supply and RETMA mounting kit | BA36R-RD |
| 180W power supply for redundant power in a BA36R (includes power cord) | CK-BA35X-HH |
| Shelves supported in M-series Cabinets with trim kit (H9A11) |
| StorageWorks UltraSCSI single bus, single-ended shelf with 180W power supply and RETMA mounting kit, blue bezel | BA35C-AA |
| StorageWorks UltraSCSI split bus, single-ended shelf with 180W power supply and RETMA mounting kit, blue bezel | BA35C-BA |
| Cabinet Front Door ( Required selection of door based on cabinet height |
| Front door, top gun blue, for H9A11-MC/MD cabinet enclosure: selection of front door for H9A11 is optional, cabinet includes front trim kit and filler bezel | H9C11-EB |
| Front door, top gun blue, for H9A10-MC/MD cabinet enclosure | H9C10-TF |
| Front door, top gun blue, for H9A15-MC/MD cabinet enclosure | H9C15-TF |
| Factory Integration ( Required |
| Factory Integration of systems and storage devices assembled and configured in cabinet enclosure in H9A10 or H9A15 cabinet enclosures | YS-ASCAA-AA |
| Factory Integration of systems and storage devices assembled and configured in cabinet enclosure for H9A11 cabinet enclosures | YS-ASCAA-AB |
| Ballast Kit |
| Ballast is added to a cabinet at particular locations for specific configurations to meet safety regulations for installation, operation, and service; see Cabinet Configuration Charts in Step 5. |
| Two 35-40 lb. steel plates | H9C10-MC |
| Compaq CustomSystems Support |
| Cabinets containing systems and storage must be assembled by qualified assemblers: Compaq Manufacturing, Compaq CustomSystems, or an authorized Compaq Certified Integration Partner. For custom integration of systems, options, cabinet expansion offerings, and additional Compaq and third party devices, or for other cabinets, doors, and trim kits of a different color, contact Compaq CustomSystems at 1-800-AT COMPAQ, or your local authorized Compaq Certified Integration Partner. |
| Step 6 ( External Storage ( Optional |
| UltraSCSI Configuration Rules |
| UltraSCSI configurations require UltraSCSI components (controllers, adapters, shelves, disks, and cables) |
| UltraSCSI adapters and RAID controllers support UltraSCSI disks at UltraSCSI speeds in UltraSCSI top gun blue shelves (DS-BA356-xx) |
| UltraSCSI StorageWorks Pedestals |
| UltraSCSI top gun blue pedestals provide support for UltraSCSI disk drives; pedestal is available in single-bus or split-bus configurations and includes a personality module and 180W power supply |
| UltraSCSI shelf supports: seven 3.5( hard disk drives, or one 5.25( device and four 3.5( hard disk drives, or two 5.25( devices and one 3.5( hard disk drive |
| Installation of redundant power supply reduces number of 3.5( drive slots by one |
| UltraSCSI single-ended pedestal, single-bus personality module, 180W power supply | DS-BA356-KF |
| UltraSCSI single-ended pedestal, split-bus personality module, 180W power supply | DS-BA356-KG |
| UltraSCSI pedestal, single-channel differential personality module, 180W power supply | DS-BA356-KH |
| 180W power supply, or redundant power, includes 120V North American and 240V IEC power cord | CK-BA35X-HH |
| Tabletop Tape Drives |
| Tape drives require single-ended UltraSCSI adapter and country-specific power cord |
| 12/24-GB 4-mm DAT narrow single-ended tabletop SCSI tape, includes 120V North American power cord, requires BN31W-xx SCSI cable | DS-TLZ10-DB |
| 20/40-GB SCSI (DLT 4000E) tabletop drive (Tru64 UNIX and OpenVMS only) | TZ88N-TA |
| 50/100-GB US AIT tabletop tape drive | 157767-001 |
| 50/100-GB International AIT tabletop tape drive | 157767-B31 |
| Storage Controllers/Adapters for External StorageWorks Shelves |
| Storage controllers require Tru64 UNIX V4.0F or OpenVMS V7.1-2 |
|  | Maximum # Supported |  |
|  | Tru64 UNIX | OpenVMS | Linux |  |
| PCI Fibre Channel adapter (KGPSA-BC), (uses one slot) | 1 | 1 | - | 380574-001 |
| Fibre Channel cable (BNGBX-xx) xx=02, 05, 15, 30, 50 meters x = 1, 2, 3, 4, 5 |  | 234457-B2x |
| PCI 2-port UltraSCSI single-ended adapter and 10/100 Mb Ethernet combo adapter (uses one PCI slot); includes internal 68-pin and 50-pin HD connectors and two external 68-pin VHDCI SCSI connectors, requires BN37A-xx cable to connect to single-ended UltraSCSI shelf | 1 | 1 | - | KZPCM-DA |
| VHDCI male-to-VHDCI male UltraSCSI cable, xx = 02, 2E [2.5], 03, 05, 10, 20 m |  | BN37A-xx |
| PCI 1-port UltraSCSI single-ended adapter, 68-pin HD connector, requires BN38C cable (2 to 20 m) to connect to single-ended UltraSCSI shelf | 1 | 1 | 1 | 3X-KZPCA-AA |
| 68-pin HD male-to-VHDCI male UltraSCSI cable; xx = 02, 03, 05, 10, 20 m |  | BN38C-xx |
| PCI 1-port UltraSCSI single-ended adapter (uses one PCI slot); includes internal 68-pin and 50-pin HD connectors and external 68-pin HD connector, requires BN38C-xx cable (2 to 20 m) to connect to single-ended UltraSCSI shelf | 1 | 1 | 1 | KZPBA-CA |
| PCI 1-port UltraSCSI differential adapter (uses one PCI slot); includes external 68-pin HD connector, requires BN38C-xx cable (2 to 25 m) to connect adapter to differential UltraSCSI shelf or RAID controller | 1 | 1 | 1 | KZPBA-CB |
| 68-pin HD male-to-VHDCI male UltraSCSI cable; xx = 02, 03, 05, 10, 20, 25 m |  | BN38C-xx |
| PCI 1-port UltraSCSI RAID controller with 4-MB cache memory (uses one PCI slot), includes RAID Array 230/Plus Subsystem software and documentation kit; includes VHDCI female connector; tape drives not supported; 18.2-GB disk drives not supported, requires BN37A-xx cable (.3 to 20 m) to connect to single-ended UltraSCSI shelf | 1 | 1 | - | KZPAC-AA |
| PCI 3-port UltraSCSI RAID controller with 4-MB cache memory (uses one PCI slot), includes RAID Array 230/Plus Subsystem software and documentation kit; includes VHDCI female connector; tape drives not supported; 18.2-GB disk drives not supported, requires BN37A-xx cable (.3 to 20 m) to connect to single-ended UltraSCSI shelf | 1 | 1 | - | KZPAC-CA |
| Same as KZPAC-CA with 8-MB cache memory | 2 | 2 | - | KZPAC-CB |
| Cache battery backup for KZPAC controller |  | KZPSC-UB |
| Factory configured RAID of KZPAC with StorageWorks shelves Note: Factory configured RAID sets for disks in single-bus StorageWorks shelves connected to KZPAC require completion of questionnaire located at http://www.digital.com/alphaserver/fcr |  | YS-ASDRD-BA |
| VHDCI male-to-VHDCI male UltraSCSI cable; xx = 02, 2E [2.5], 03, 05, 10, 20, 25 m Note: Manufacturing may substitute BN37A-02 cable for specific cabinet configurations. |  | BN37A-xx |
| SCSI cable/bulkhead assembly kit, supports one third-port connection from KZPAC-CA/CB, allows external connection of one third port |  | BN31K-0E |
| SCSI cable/bulkhead assembly kit, supports two third-port connections from KZPAC-CA/CB, allows external connection of two third ports |  | KZPAC-SB |
| BA370 Rackmount Enclosure |
| M-series cabinets (H9A10 and H9A15) allow one BA370 enclosure to be installed in front cabinet |
| Host adapter, RAID Array controller, platform specific Solutions Software Kit, and disk drives must be ordered separately |
| BA370 front mount rackmount enclosure with five 180W power supplies, includes RETMA rackmount kit; first BA370 enclosure must be front mounted in cabinet, 20U height | 2T-BA370-AS |
| Factory configured RAID of rackmounted BA370/HSZ80 | YS-ASCRD-AA |
| Note: Factory configured RAID sets for disks in rackmounted BA370 StorageWorks shelf controlled by one or two HSZ70s require completion of questionnaire located at http://www.digital.com/alphaserver/fcr |
| Removable Media Devices for External StorageWorks Shelves |
| 12/24-GB 4 mm DAT narrow SCSI tape drive in StorageWorks carrier | DS-TLZ10-VA |
| 35/70-GB AIT tape drive in StorageWorks carrier (Tru64 UNIX and OpenVMS only) | DS-AIT35-VW |
| 600-MB 32X CD-ROM drive in StorageWorks carrier | DS-RRD47-VA |
| StorageWorks Shelf ( Requires selection of UltraSCSI adapter and SCSI cable |
| StorageWorks UltraSCSI single-bus shelf kit | BA36R-RC |
| StorageWorks UltraSCSI split-bus shelf kit | BA36R-RD |
| External Storage Disk Drive (Supported in StorageWorks Shelf) |
| Maximum six (10,000 rpm) or seven (7,200 rpm) drives supported in StorageWorks shelf |
| One power supply supports a maximum of six 10,000 rpm disks |
| 9.1-GB 7200 RPM Ultra2 SCSI drive | DS-RZ1DA-VW |
| 18.2-GB 7200 RPM Ultra2 SCSI drive | DS-RZ1EA-VW |
| 36.4-GB 7200 RPM Ultra2 SCSI drive | DS-RZ1FB-VW |
| 9.1-GB 10000 RPM Ultra2 SCSI drive | DS-RZ1DD-VW |
| 18.2-GB 10000 RPM Ultra2 SCSI drive | DS-RZ1ED-VW |
| 36.4-GB 10000 rpm Ultra2 SCSI drive | DS-RZ1FC-VW |
| Step 7 (UltraSCSI RAID Array Controllers and UltraSCSI RAID Packaged Solutions ( Optional |
| RAID Array 3000 Rackmount Controller Shelf |
| Selection of RA3000 Solutions Software Kit is required |
| Supported SCSI adapter: KZPBA-CB PCI 1-port UltraSCSI differential adapter |
| RA3000 rackmount controller shelf, blue, with one controller, 110V Includes: UltraSCSI BA356 controller shelf, one HSZ22 2-channel controller with 16-MB cache, integrated Environmental Monitoring Unit (EMU), two 180W power supplies, two dual-port host differential UltraSCSI I/O SBBs, dual-channel UltraSCSI single-ended personality modules, one 120V 1000VA rackmount UPS, 5-m host SCSI cable (BN37A-05), BN38E-0B adapter, UPS serial cable, PC connection serial cable (DB-9), two 68-pin HD tri-link adapters (H8861-AA), two North American power cords, and RETMA mounting bracket (disk shelves and disks not included) Requires: Solutions Software Kit for platform, host adapter, RA3000 disk shelf, and disks Options: Second HSZ22 controller, up to four additional RA3000 disk shelves, cache memory upgrade | DS-SWXRA-GH |
| RA3000 rackmount controller shelf, blue, with one controller, 230V Includes: UltraSCSI BA356 controller shelf, one HSZ22 2-channel controller with 16-MB cache, integrated Environmental Monitoring Unit (EMU), two 180W power supplies, two dual-port host differential UltraSCSI I/O SBBs, dual-channel UltraSCSI single-ended personality modules, one 230V 1000VA rackmount UPS, 5-m host SCSI cable (BN37A-05), BN38E-0B adapter, UPS serial cable, PC connection serial cable (DB-9), two 68-pin HD tri-link adapters (H8861-AA), RETMA mounting bracket (disk shelves and disks not included) Requires: Solutions Software Kit for platform, two country-specific power cords, host adapter, RA3000 disk shelf, and disks Options: Second HSZ22 controller, up to four additional RA3000 disk shelves, cache memory upgrade | DS-SWXRA-GK |
| RAID Array 3000 Rackmount Disk Shelf |
| Select one to four disk shelves |
| Third and fourth DS-SWXRA-GN disk shelf ordered will be installed in rear of M-series cabinet; rear mounted shelves require that a 2-m BN37A-02 SCSI cable be ordered |
| RA3000 rackmount disk shelf, blue, includes UltraSCSI BA356 disk shelf, two 180 W power supplies, single-ended UltraSCSI personality card, one half meter SCSI cable (BN37A-0E), two North American power cords, and RETMA mounting bracket (disks not included); order two country-specific power cords for non-North American use | DS-SWXRA-GN |
| HSZ22 Controller |
| Note that second HSZ22 controller ordered is field installed only, not factory installed; requires BN37A-0E SCSI jumper cable be ordered separately |
| Second HSZ22 controller with 16-MB cache and two 16-MB SIMMs for mirror cache, one BN37A-05 5-m UltraSCSI cable, one BN38E-0B cable adapter ( field installable only; note that second HSZ22 controller does not require additional Solution Software Kit | DS-HSZ22-AA |
| Second HSZ22 controller with 32-MB cache and two 32-MB SIMMs for mirror cache, one BN37A-05 5-m UltraSCSI cable, one BN38E-0B cable adapter ( field installed only; note that second HSZ22 controller does not require additional Solution Software Kit | DS-HSZ22-AB |
| RA3000 Solutions Software Kit |
| StorageWorks Command Console (SWCC) software |
| Platform specific software |
| Installation scripts and installation documentation |
| RA3000 Solutions Software Kit for Tru64 UNIX | QB-5TWAB-SA |
| RA3000 Solutions Software Kit for OpenVMS | QB-5TWAC-SA |
| HSG80/HSZ80 External Controllers |
| Fibre Channel controller (DS-HSG80-BJ), includes 2-MB cache expandable to 128 MB; requires 128697-B21 HSG80 ACS V8.4F software kit or 128698-B21 V8.4P software kit for each HSG80 ordered | 380672-B21 |
| Fibre Channel controller (DS-HSG80-BH), includes 64-MB cache expandable to 128 MB; requires 128697-B21 HSG80 ACS V8.4F software kit or 128698-B21 V8.4P software kit for each HSG80 ordered | 380671-B21 |
| UltraSCSI controller (DS-HSZ80-AH), includes 64-MB cache expandable to 128 MB; requires 400569-001 for Tru64 UNIX or 400571-001 for OpenVMS | 400564-B21 |
| UltraSCSI controller (DS-HSZ80-AJ), includes 256-MB cache expandable to 512 MB; requires 400569-001 for Tru64 UNIX or 400571-001 for OpenVMS | 400565-B21 |
| ESA 10000 , RAID Array 7000, RAID Array 8000 |
| Enterprise Storage Array 10000 and RAID Array 7000 (HSZ70) product set are supported on AlphaServer DS10L systems |
| Supported SCSI adapter for HSZ80/HSZ70 ( KZPBA-CB PCI 1-port UltraSCSI differential adapter |
| Supported SCSI adapter for HSG80 ( KGPSA-BC PCI 1-port Fiber-Channel adapter |
| Step 8 ( Graphics Adapters ( Optional |
| RAID Configuration Utility is accessible via console port for Tru64 UNIX and OpenVMS systems; optional graphics capability available |
| Select graphics adapter, monitor, and country-specific keyboard if required |
|  | Maximum # Supported |  |
|  | Tru64 UNIX | OpenVMS | Linux |  |
| ELSA Gloria synergy graphics with 8-MB SGRAM 1600 x 1200, 2D/3D graphics accelerator | 1 | 1 | 1 | SN-PBXGK-BB |
| Step 9 (Monitors (Optional |
| Graphics monitors other than those listed can be used if compatible with SVGA graphics ordered with system |
| Selection of video cable and country-specific power cord is mandatory for all monitors |
| AlphaServer DS10L has been designed for desktop use and will support a 21” monitor |
| 15( Corporate Series auto-scan color monitor, VGA to 1024 x 768 @ 85 Hz; Northern Hemisphere without power cord | 3R-VRQV5-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQV5-11 |
| 17( (16.0( viewable image size) professional series auto-scanning color monitor, Trinitron CRT, 0.25 mm aperture grill pitch, VGA to 1280 x 1024 @75 Hz, TCO 99, MPR-II, Energy Star, attached 1.8-m video cable; Northern Hemisphere without power cord | 3R-VRQP7-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQP7-23 |
| 19( (16( viewable image size) professional series auto-scanning color monitor, Trinitron CRT, 0.25 mm aperture grill pitch, VGA to 1280 x 1024 at 75 Hz, TCO 95, MPR-II, Energy Star, attached 1.8-m video cable; Northern Hemisphere without power cord | 3R-VRQP9-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQP9-23 |
| 21( (19.6( viewable image size) auto-scanning color monitor, Trinitron CRT, 0.28 mm aperture grill pitch, VGA to 1600 x 1200 @85 Hz NI, TCO 95, Energy Star, includes 1.8-m video cable; Northern Hemisphere without power cord | 3R-VRQP1-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQP1-23 |
| Video Cable |
| 1.8-m video cable — mandatory for each monitor ordered | BN39C-02 |
| Monitor Power Cords |
| North American, 120V, 75( | BN26J-1K |
| Australia, New Zealand, 2.5m | BN19H-2E |
| Central Europe, 2.5m | BN19C-2E |
| UK, Ireland, 2.5m | BN19A-2E |
| UK, Ireland, 2.5m | BN19A-2E |
| Switzerland, 2.5m | BN19E-2E |
| Denmark, 2.5m | BN19K-2E |
| Italy, 2.5m | BN19M-2E |
| Egypt, India, South Africa, 2.5m | BN19S-2E |
| Israel, 2.5m | BN18L-2E |
| Japan, 2.5m | 3X-BN46F-02 |
| Step 10 ( Networks and Communications ( Optional |
| Systems include dual embedded 10/100 BaseT Ethernet ports (BN25G-xx cable must be ordered separately) |
| Additional Ethernet ports can be added using available PCI slots |
|  | Maximum # Supported |  |
|  | Tru64 UNIX | OpenVMS | Linux |  |
| PCI 1-port 10/100-Mb Ethernet adapter (Twisted Pair) | 1 | 1 | 1 | 3X-DE600-AA |
| PCI 2-port 10/100-Mb Ethernet adapter (Twisted Pair) | 1 | 1 | 1 | 3X-DE602-AA |
| SC-SC Dual fibre optic cable, mm, pp xx = length in meters |  | BN34B-xx |
| PCI 2-port 10/100 Mbit, Fast Ethernet adapter, UTP | - | 1 | 1 | 3X-DE602-FA |
| PCI 10/100 Mbit 4-port Ethernet adapter, UTP | 1 | 1 | 1 | DE504-BA |
| Cable for 10BaseT twisted pair connection |  | BN25G-xx |
| PCI Gigabit Ethernet adapter, SC connectors, MMF, no boot support | 1 | 1 | 1 | DEGPA-SA |
| SC-to-SC dual fiber optic cable |  | BN34B-xx |
| PCI FDDI adapter, single attachment station (SAS), multi-mode fiber (MMF), SC connector | 1 | - | - | 3X-DEFPA-AC |
| PCI FDDI adapter, DAS, MMF, SC connector | 1 | - | - | 3X-DEFPA-DC |
| MIC-SC dual fiber optic cable mm, pp xx = length in meters |  | BN34D-xx |
| SC-to-SC dual fiber optic cable mm, pp xx = length in meters |  | BN34B-xx |
| PCI FDDI adapter, SAS, TP-PMD, requires BN25H-03 cable | 1 | - | - | 3X-DEFPA-UC |
| PCI FDDI dual adapter, DAS, TP-PMD, requires BN25H-03 cable | 1 | - | - | 3X-DEFPA-MC |
| 3m (9.8") FDDI cross-over cable mm, pp xx = length in meters |  | BN25H-03 |
| PCI 4-port asynchronous controller; maximum two PBXDA-xx controllers per system | 1 | 1 | - | PBXDA-AA |
| PCI 8-port asynchronous controller, cable included; maximum two PBXDA-xx controllers per system | 1 | 1 | - | PBXDA-AB |
| PCI 16-port asynchronous controller, cable included; maximum two PBXDA-xx controllers per system | 1 | 1 | - | PBXDA-AC |
| Step 11 (Keyboards |
| Keyboards are not included with system and must be ordered separately |
|  | Tru64 UNIX or Linux | OpenVMS |
| U.S./English keyboard | SN-LKQ47-AA | LK461-A2 |
| Belgian keyboard | SN-LKQ47-AB | LK461-AB |
| Canadian/French keyboard | SN-LKQ47-AC | LK461-AC |
| Danish keyboard | SN-LKQ47-AD | LK461-AD |
| UK keyboard | SN-LKQ47-AE | - |
| Finnish keyboard | SN-LKQ47-AF | LK461-AF |
| German keyboard | SN-LKQ47-AG | LK461-AG |
| Dutch keyboard | SN-LKQ47-AH | LK461-AH |
| Italian keyboard | SN-LKQ47-AI | LK461-AI |
| Swiss/French keyboard | SN-LKQ47-AK | LK461-AK |
| Swiss/German keyboard | - | LK461-AL |
| Swedish keyboard | SN-LKQ47-AM | LK461-AM |
| Norwegian keyboard | SN-LKQ47-AN | LK461-AN |
| French keyboard | SN-LKQ47-AP | LK461-AP |
| Canadian/English keyboard | - | LK461-AQ |
| Latin-American keyboard | SN-LKQ47-AR | - |
| Spanish keyboard | SN-LKQ47-AS | LK461-AS |
| Hebrew keyboard | SN-LKQ47-AT | LK461-AT |
| Portuguese keyboard | SN-LKQ47-AV | LK461-AV |
| BHCSY keyboard | SN-LKQ47-AX | - |
| International keyboard | SN-LKQ47-BA | - |
| Greek keyboard | SN-LKQ47-BH | LK461-BH |
| Taiwanese keyboard | SN-LKQ47-BI | - |
| Korean keyboard | SN-LKQ47-BK | - |
| Romanian keyboard | - | LK461-BL |
| Polish keyboard | SN-LKQ47-BP | LK461-BP |
| Hungarian keyboard | SN-LKQ47-BQ | LK461-BQ |
| Arabic keyboard | SN-LKQ47-BR | - |
| Cyrillic keyboard | SN-LKQ47-BT | LK461-BT |
| Turkish keyboard | SN-LKQ47-BU | LK461-BU |
| Czech keyboard | SN-LKQ47-BV | LK461-BV |
| Turkish/French keyboard | - | LK461-BW |
| Yugoslavian keyboard | - | LK461-BY |
| Thai keyboard | SN-LKQ47-CB | - |
| S. Chinese keyboard | SN-LKQ47-CV | - |
| Slovak keyboard | SN-LKQ47-CZ | LK461-CZ |
| Keyboard or Mouse Extension Cable |
| 6 ft keyboard or mouse extension cable; to extend both keyboard and mouse order two cables | 17-04016-01 |
| Mouse |
| Standard Compaq opal mouse | SN-PBQWS-WA |
| Step 12 ( Console Terminal ( Optional |
| Any terminal can be used as a console device |
| Third-party console devices require an EIA-232 25-pin DSUB connector |
| VT510 video terminal; requires H857-x cable, either male or female | VT510-xx |
| Console cable, female connector | H857-A |
| Console cable, male connector | H857-D |
| Console cable, male connector (IBM compatible) | H897-E |
| Step 13 ( Software ( Required selection of media and documentation for first system on site |
| Software Processor Code = E |
| Tru64 UNIX |
| Tru64 UNIX systems include Tru64 UNIX Traditional Unlimited User license, Server Extension, Internet Access Software kit, and Netscape's Enterprise Server 3.0 |
| Tru64 UNIX media and online documentation on CD-ROM | QA-MT4AA-H8 |
| Tru64 UNIX full hard copy documentation | QA-MT4AA-GZ |
| StorageWorks Software Package, includes licenses for Logical Storage Manager and AdvFS Utilities | QB-5RXAE-AA |
| TruCluster Available Server License | QL-05SAE-AA |
| Advanced Server for Tru64 UNIX, 25 client concurrent use license | QL-5U29M-3D |
| Advanced Server for Tru64 UNIX, 50 client concurrent use license | QL-5U29M-3E |
| Advanced Server for Tru64 UNIX, 100 client concurrent use license | QL-5U29M-3F |
| Advanced Server for Tru64 UNIX, 250 client concurrent use license | QL-5U29M-3G |
| Advanced Server for Tru64 UNIX, 500 client concurrent use license | QL-5U29M-3H |
| Layered products media and documentation for Tru64 UNIX on CD-ROM | QA-054AA-H8 |
| DECnet/OSI end-system license for Tru64 UNIX | QL-MTJAE-AA |
| DECnet/OSI extended function license for Tru64 UNIX | QL-MTKAE-AA |
| OpenVMS |
| OpenVMS systems include OpenVMS base license, TCP/IP Services for OpenVMS, DECWindows Motif for OpenVMS Alpha, DECnet Plus for OpenVMS End System, and Pathworks 32 |
| OpenVMS Concurrent Use Licenses are not specific to a single system and can be moved between systems at user discretion; OpenVMS Concurrent Use Licenses can also be shared in a mixed OpenVMS VAX and OpenVMS Alpha Cluster |
| Concurrent Use 1-user license | QL-MT3AA-3B |
| Concurrent Use 2-user license | QL-MT3AA-3C |
| Concurrent Use 4-user license | QL-MT3AA-3D |
| Concurrent Use 8-user license | QL-MT3AA-3E |
| Concurrent Use 16-user license | QL-MT3AA-3F |
| Concurrent Use 32-user license | QL-MT3AA-3G |
| Concurrent Use 64-user license | QL-MT3AA-3H |
| Concurrent Use 128-user license | QL-MT3AA-3J |
| Concurrent Use 256-user license | QL-MT3AA-3K |
| Traditional unlimited user license | QL-MT2AQ-AA |
| OpenVMS media and documentation on CD-ROM | QA-MT1AA-H8 |
| OpenVMS full hard copy documentation | QA-001AA-GZ |
| Layered products media and documentation for OpenVMS on CD-ROM, includes Enterprise Integration Server for OpenVMS media and documentation | QA-03XAA-H8 |
| DIGITAL Enterprise Integration Server for OpenVMS media and documentation | QA-5LVAA-H8 |
| DECnet extended function license for OpenVMS | QL-MTGAE -AA |
| DECnet end-system to extended function upgrade license for OpenVMS | QL-MTHAE-AA |
| OpenVMS Cluster license for Alpha systems | QL-MUZAE-AA |
| OpenVMS Volume Shadowing license | QL-2A1AE-AA |
| Note: Linux-Ready systems ship without system software; Red Hat 6.0 or SuSe 6.1 Linux may be purchased separately from a Linux distributor. |
| Step 14 ( Hardware and Software Supplemental Support Services |
| Systems include 1-year hardware warranty, on-site, with 5 x 9, 24-hour response time; select optional Hardware Supplemental Support Services if required |
| Options ordered as part of "Initial System Sale" take on warranty of the enclosure; options added after "Initial System Sale" take on warranty of enclosure until enclosure warranty ends |
| All unique AlphaServer DS10L options have a minimum of 1-year Return-to-Compaq warranty |
| Hardware Supplemental Support ( Americas and Asia Pacific only |
| 3-year, 5 x 9, 4-hour response time | FM-MK4HR-36 |
| 5-year, 5 x 9, 4-hour response time | FM-MK4HR-60 |
| 3-year, 5 x 12, 4-hour response time | FM-MK512-36 |
| 5-year, 5 x 12, 4-hour response time | FM-MK512-60 |
| 3-year, 6 x 16, 4-hour response time | FM-MK616-36 |
| 5-year, 6 x 16, 4-hour response time | FM-MK616-60 |
| 3-year, 7 x 24, 4-hour response time | FM-MK724-36 |
| 5-year, 7 x 24, 4-hour response time | FM-MK724-60 |
| 5-year, 7 x 24, 4-hour response time | FM-MK724-60 |
| Years 4-5, 5 x 9, next day response time | FM-MKXHW-60 |
| Installation Services |
| Hardware product installation for AlphaServer DS10L | FM-TC12X-IN |
| Add-on memory installation for AlphaServer DS10L | FM-TCMEM-IN |
| Add-on CPU installation for AlphaServer DS10L | FM-TCSMP-IN |
| Software Supplemental Support ( Americas and Asia Pacific only |
| Systems include 90-day Conformance to SPD and Telephone Advisory Support; select optional Software Supplemental Support Services if required |
| Software service upgrades for Tru64 UNIX include advisory and remedial software support with new version license rights for operating system for time period indicated |
| Software service upgrades for OpenVMS include advisory and remedial software support with new version license rights for operating system and Enterprise Integration Package for time period indicated |
| Software service upgrades for SMP upgrades running Tru64 UNIX or OpenVMS include new version license rights for Tru64 UNIX or OpenVMS SMP Upgrades for time period indicated; one required for each SMP upgrade |
| Software Supplemental Services | Tru64 UNIX | OpenVMS |
| 1-year, 5 x 9 Bronze Software Supplemental Support | FM-D10U9-12 | FM-D10V9-12 |
| 3-year, 5 x 9 Bronze Software Supplemental Support | FM-D10U9-36 | FM-D10V9-36 |
| 5-year, 5 x 9 Bronze Software Supplemental Support | FM-D10U9-60 | FM-D10V9-60 |
| 1-year, 7 x 24 Bronze Software Supplemental Support | FM-D10US-12 | FM-D10VS-12 |
| 3-year, 7 x 24 Bronze Software Supplemental Support | FM-D10US-36 | FM-D10VS-36 |
| 5-year, 7 x 24 Bronze Software Supplemental Support | FM-D10US-60 | FM-D10VS-60 |
| 1-year, Bronze Node Software Supplemental Support | FM-D10UN-12 | FM-D10VN-12 |
| 3-year, Bronze Node Software Supplemental Support | FM-D10UN-36 | FM-D10VN-36 |
| 5-year, Bronze Node Software Supplemental Support | FM-D10UN-60 | FM-D10VN-60 |

| Physical Characteristics |  | Dimensions (WxDxH) | 17.5 x 20.5 x 1.7 in / 44.5 x 52 x 4.3 cm |
| --- | --- | --- | --- |
|  |  | Shipping Dimensions | 23.6 x 21.7 x 10.1 in / 60 x 55 x 26 cm |
|  |  | Weight | 21 lbs / 9.4 kg |
| Cabinets |  |  | H9A10 M-Series | H9A15 M-Series |
|  |  | Dimensions (HxWxD) | 67 x 23.6 x 43.27 in/ 170 x 60 x 110 cm | 79 x 23.6 x 35.4 in 200 x 60 x 90 cm |
|  |  | Shipping Dimensions | 73 x 36 x 48 in / 185.5 x 91.5 x 122 cm | 85 x 36 x 48 in / 216 x 91.5 x 122 cm |
|  |  | Weight | Configuration dependent | 1000 lbs / 450 kg |
|  |  | Shipping Weight | Configuration dependent, maximum payload 1,000 lbs | 1056 lbs / 550 kg (normal) 1,408 lbs / 640 kg (maximum) |
| System Unit |  | Environmental |  |
|  |  | Temperature |  |
|  |  | Operating (Tower, Rackmount)1 | 50( to 95(F / 10( to 35(C |
|  |  | Non-operating | 41 to 122 F / 5 to 50C |
|  |  | Storage (60 days) | –40( to –151(F / –40 to –66(C |
|  |  | Rate of change | 20(F/hr / 11(C/hr |
|  |  | Relative Humidity |  |
|  |  | Operating | 10% to 90% RH |
|  |  | Non-operating | 10% to 95% |
|  |  | Storage (60 days) | 10% to 95% |
|  |  | Maximum Wet Bulb Temperature |  |
|  |  | Operating | 82(F / 28(C |
|  |  | Non-operating | 90(F / 32(C |
|  |  | Storage (60 days) | 115(F / 46(C |
|  |  | Heat Dissipation |  |
|  |  | H9A10/H9A15 Cabinets | Configuration dependent |
|  |  | Air Flow and Quality |  |
|  |  | Intake location | Front |
|  |  | Exhaust location | Rear pedestal and rack |
|  |  | Particle size | N/A |
|  |  | Concentration | N/A |
|  |  | Altitude |  |
|  |  | Operating 2 | 10,000 f/3,037m |
|  |  | Non-operating | 40,000 ft/12,192m |
|  |  | Acoustics (Declared values per ISO 9296 and ISO 7779) |
|  |  | Acoustics 3 | LWAd3B | LnAm5dBA (bystander position) |
|  |  | Idle | 6.0 | 46 |
|  |  | Operating | 6.1 | 47 |
|  |  | Vibration |  |
|  |  | Operating | 5-500 Hz at .1 G peak (limited by 0.02”/0.5mm double amplitude) |
|  |  | Non-operating | 1.03 Grms 5-300 Hz |
|  |  | Shock |  |
|  |  | Operating | 10 G 10ms half-sine |
| System Unit (continued) |  | Electrical (Power supplies are universal, PFC, auto ranging, 100/240 Vac) |
|  |  | Nominal Voltage (Vac) | 100 | 120 | 200-240 |
|  |  | Voltage Range (Vac) (temporary condition) | 90-100 | 110-128 | 180-250 |
|  |  | Power Source Phase | Single | Single | Single |
|  |  | Nominal Frequency (Hz) | 50/60 | 50/60 | 50/60 |
|  |  | Frequency Range (Hz) | 49 to 51/59 to 61 | 49 to 51/59 to 61 | 49 to 51/59 to 61 |
|  |  | RMS Current (maximum steady state) |  |  |  |
|  |  | Single power cord | 2.3A | 1.9A | 1.1A |
|  |  | Maximum VA | 230 | 229 | 220 |
|  |  | M-series Cabinet (configuration dependent) |  |  |  |
|  |  | Nominal voltage (Vac) | 100 | 120 | 220-240 |
|  |  | Each power cord | 24A | 24A | 16A |
|  |  | Power Cords |  |  |
|  |  | Pedestal | 1 (75 in / 190 cm) | IEC 320 C13 to NEMA 5-15 (N. America) or IEC 320 C13 to country-specific |
|  |  | Rackmount | 1 (14 ft 10 in / 452 cm) | IEC 320 C13 to NEMA 5-15 (N. America) or IEC 320 C13 to IEC 320 C14 (other countries) |
|  |  | Cabinet | 2 (10 ft 10 in / 330 cm) | 120V non-removable NEMA L5-30P or 200-240V non-removable IEC 309 |
|  |  | Regulatory |  |
|  |  | Agency Approvals | UL: Listed to UL1950 (3rd edition) |
|  |  |  | CUL Listed: CAN/CSA-C22.2 No. 950-M95 |
|  |  |  | TUV: EN 60950/A11: 1997 GS marked |
|  |  |  | FCC: Part 15.B Class A |
|  |  |  | CE: EN55022, EN50082 |
|  |  |  | VCCI Class II ITE |
|  |  |  | BMSI: CISPR22, CNS13438 |
|  |  |  | C-Tick: CISPR22, AS/NZS 3548 |
|  |  | Reviewed to | AS/NZ 3260:1993 Australian/New Zealand Standard |
|  |  |  | EN 60950/A11: 1997 European Norm |
|  |  |  | IEC950 (2nd edition, 4th amend) |

Maximum operating temperature at sea level; reduce by 1.8(F (1(C) for each 600m (2,000 ft) above sea level.

Higher altitudes are possible if maximum operating temperature is reduced (see Temperature); other restrictions may apply such as maximum permissible altitude for hard drives.

Current values for specific configurations are available from Compaq, note that 1 B = 10 dBA.

# Text boxes

Revision 4.0

March  13, 2000

Fan

CPU and fan

Power supply

Memory boards

Diskette/CD-ROM drive

Fans

Disk

PCI riser card

Dual Ethernet ports

Keyboard and mouse ports

At A Glance

AlphaServer DS10L Systems include:

1U Alpha processor module with 21264 466-MHz CPU with 2-MB onboard ECC cache

Onboard IDE controller for internal storage

Onboard dual 10/100 BaseT Ethernet ports

One full-length PCI expansion slot

1-GB maximum memory capacity

Optional combo 1.44-MB diskette drive/CD-ROM drive, or 3.5( x 1( hard disk drive bay

Optional rackmount kit for single or quad configurations

Two serial ports, one with full-duplex asynchronous modem control, one RMC dedicated serial port with full-duplex asynchronous modem control

Bi-directional enhanced parallel port

Dual USB ports (future support)

PS/2-style keyboard port and mouse port

150W (120/240V, 60/50 Hz) power supply

Integral remote system management console

U.S. English documentation

Tru64( UNIX or OpenVMS Factory Installed Software with 90-day software product warranty

Protected by Compaq Services, including one-year, on-site hardware with next business day response