| Processor |
| --- |
| Alpha 21264 500 MHz or 667 MHz processor |
| Cache Memory |
| 4-MB level 2 writeback cache per 500 MHz processor 8-MB level 2 Dual Data Rate cache per 667 MHz processor |
| Upgradability |
| System upgradable to dual processing |
| Memory |
| Standard | 256-MB, 512-MB, or 1-GB ECC SDRAM memory standard |
| Maximum | 4 GB |
| Network Controller |
| Choice of Ethernet controllers |
| Expansion |
| I/O (Total) | 6 |
| PCI | 5 |
| Shared PCI/ISA | 1 |
| Storage Controller |
| Choice of storage controllers |
| Storage |
| Diskette Drive | 1.44 MB |
| CD-ROM | 24X Max IDE CD-ROM Drive |
| Internal Hard Drives | Choice of 9.1 GB, or 18.2 GB |
| Maximum Internal Storage | 72 GB |
| Expansion Ports |
| Parallel | 1 |
| Serial | 2 |
| Pointing Device (Mouse) | 1 |
| Keyboard | 1 |
| SCSI knockouts on rear of chassis | 4 |
| USB | 2 (future support) |
| Form Factor |
| Rackmount or Tower |
| Manageability |
| Compaq Insight Manager |
| Hot plug redundant power supply support; hot plug fan support |
| Power Supply |
| Two 375-Watt Hot Plug Power Supplies, standard; optional third N+1 for redundancy |
| OS Support |
| Tru64 UNIX AlphaServers include pre-installed software, base license, unlimited user license, server extension license, Open Source Internet Solutions, and Netscape Enterprise Server 3.0. Tru64 UNIX AlphaStations include a base 2-user and Compaq Open3D license. OpenVMS AlphaServer include pre-installed software, base license, and Enterprise Integration Server License Package V3.0A. OpenVMS AlphaStations include an OpenVMS base license, concurrent use 1-user license, and Compaq Open3D license. Minimum OS support: Tru64 UNIX V4.0F, OpenVMS V7.1-2 or V7.2-1 |
| Service and Support |
| Compaq Services provides a wide range of service offerings including a three-year limited warranty2 fully supported by a worldwide network of resellers and service providers; lifetime toll-free 7 x 24 hardware technical phone support. |

| Step 1 ( Select system |
| --- |
| AlphaServer DS20E systems require the mandatory selection of the following items: Pedestal/tower or rackmount bezel kit Disk drive cage Ultra2 SCSI adapter System disk drive Ethernet adapter Power cord Software media and documentation for first system onsite Notes: DS20E minimum OS support (Tru64 UNIX V4.0F, OpenVMS V7.1-2 or V7.2-1 Keyboard not included For system integration of options with 6-3 part numbers, contact CustomSystems |
| AlphaServers |
| OS | CPU | Memory / Cache | Order No. |
| Tru64 UNIX | 500 MHz | 256 MB / 4MB | DA-56NRA-DA |
| Tru64 UNIX | 500 MHz | 512 MB / 4MB | DA-56NRA-EA |
| Tru64 UNIX | 500 MHz | 1 GB / 4MB | DA-56NRA-FA |
| Tru64 UNIX | 667 MHz | 256 MB / 8MB | DA-56PAA-DA |
| Tru64 UNIX | 667 MHz | 512 MB / 8MB | DA-56PAA-EA |
| Tru64 UNIX | 667 MHz | 1 GB / 8MB | DA-56PAA-FA |
| OpenVMS | 500 MHz | 256 MB / 4MB | DY-56NRA-DA |
| OpenVMS | 500 MHz | 512 MB / 4MB | DY-56NRA-EA |
| OpenVMS | 500 MHz | 1 GB / 4MB | DY-56NRA-FA |
| OpenVMS | 667 MHz | 256 MB / 8MB | DY-56PAA-DA |
| OpenVMS | 667 MHz | 512 MB / 8MB | DY-56PAA-EA |
| OpenVMS | 667 MHz | 1 GB / 8MB | DY-56PAA-FA |
| AlphaStations |
| OS | CPU | Memory / Cache | Order No. |
| Tru64 UNIX | 500 MHz | 256 MB / 4MB | DA-56NRA-DW |
| Tru64 UNIX | 500 MHz | 512 MB / 4MB | DA-56NRA-EW |
| Tru64 UNIX | 500 MHz | 1 GB / 4MB | DA-56NRA-FW |
| Tru64 UNIX | 667 MHz | 256 MB / 8MB | DA-56PAA-DW |
| Tru64 UNIX | 667 MHz | 512 MB / 8MB | DA-56PAA-EW |
| Tru64 UNIX | 667 MHz | 1 GB / 8MB | DA-56PAA-FW |
| OpenVMS | 500 MHz | 256 MB / 4MB | DY-56NRA-DW |
| OpenVMS | 500 MHz | 512 MB / 4MB | DY-56NRA-EW |
| OpenVMS | 500 MHz | 1 GB / 4MB | DY-56NRA-FW |
| OpenVMS | 667 MHz | 256 MB / 8MB | DY-56PAA-DW |
| OpenVMS | 667 MHz | 512 MB / 8MB | DY-56PAA-EW |
| OpenVMS | 667 MHz | 1 GB / 8MB | DY-56PAA-FW |
| Step 2 ( Select mandatory options |
| Step 2a ( Bezel Kits ( Mandatory |
| Pedestal/Tower kit or Rackmount kit is mandatory for each system |
| Pedestal/Tower bezel kit for 500 MHz systems | 3X-BA56P-PA |
| Rackmount bezel kit (M-Series Cabinets) for 500 MHz systems | 3X-BA56R-RA |
| Pedestal/Tower bezel kit for 667 MHz systems | 3X-BA56P-PB |
| Rackmount bezel kit (M-Series Cabinets) for 667 MHz systems | 3X-BA56R-RC |
| Step 2b ( Disk Drive Cage ( Mandatory |
| Systems support one disk drive cage; disk drive cage supports four 3.5” hard disk drives |
| Each drive cage includes Ultra Universal drive height converter (4-pack) to install 1.0” Universal drives. |
| 4-bay disk drive cage | 3X-BA611-4D |
| Step 2c ( Ultra2 SCSI Adapter ( Mandatory |
| Selection of Ultra2 SCSI adapter to connect to internal disk drive cage is mandatory; SCSI cable included with system |
| Single channel LVD adapter, maximum 4 per system | 3X-KZPCA-AA |
| Step 2d( System Disk Drive (Supported in Disk Drive Cage) ( Mandatory |
| Selection of one disk drive is mandatory |
| 9.1-GB 7200 RPM 1.0( Universal Ultra2 SCSI disk drive | 3R-A0525-AA |
| 9.1-GB 10000 RPM 1.0( Universal Ultra2 SCSI disk drive | 3R-A0526-AA |
| 18.2-GB 7200 RPM 1.0( Universal Ultra2 SCSI disk drive | 3R-A0527-AA |
| 18.2-GB 10000 RPM 1.0( Universal Ultra2 SCSI disk drive | 3R-A0561-AA |
| Ultra Universal drive height converter, 4-pack (included in disk drive cage). Customers with earlier 4-slot drive cages (3X-BA611-4D) need to order separately when installing 1” Universal drives | 3R-A0528-AA |
| Step 2e ( Ethernet Adapters ( Mandatory |
| Selection of one Ethernet adapter is mandatory (Ethernet adapter is not required if KZPCM adapter is selected) |
| See Step 12 for additional networking options |
| PCI 1-port 10/100 Mbit Fast Ethernet adapter, UTP, maximum four per system | 3X-DE600-AA |
| PCI 2-port 10/100 Mbit, Fast Ethernet adapter, UTP, maximum two per system | 3X-DE602-AA |
| Multi-mode fiber (MMF) add-on daughter card for 3X-DE602-AA | 3X-DE602-FA |
| PCI 10/100 Mbit 4-port Ethernet adapter, UTP, maximum one per system | DE504-BA |
| Cable for 10BaseT twisted pair connection | BN25G-xx |

| Step 2f ( Power Cords ( Mandatory |
| --- |
| Selection of power cord is mandatory for all systems |
| Pedestal Power Cords |
| North American 120V, 75( | BN26J-1K |
| Australia, New Zealand, 2.5m | BN19H-2E |
| Central Europe, 2.5m | BN19C-2E |
| UK, Ireland, 2.5m | BN19A-2E |
| Switzerland, 2.5m | BN19E-2E |
| Denmark, 2.5m | BN19K-2E |
| Italy, 2.5m | BN19M-2E |
| Egypt, India, South Africa, 2.5m | BN19S-2E |
| Israel, 2.5m | BN18L-2E |
| Japan, 2.5m | 3X-BN46F-02 |
| Rackmount Power Cords |
| US/Canada | BN20Z-4E |
| Non-US | BN35S-4E |
| Japan, 2.5m | 3X-BN46D-4E |
| Step 3 ( Additional CPU Modules ( Optional |
| One 6/500-MHz or 6/667-MHz CPU included, one additional CPU supported. Second CPU must be the same speed. A 500 MHz system can be upgraded to 667 MHz by swapping out the 500 MHz CPU(s) |
| SMP upgrade includes one 6/500-CPU with 4-MB cache and Tru64 UNIX SMP license | KN310-BB |
| SMP upgrade includes one 6/500-CPU with 4-MB cache and OpenVMS SMP license | KN310-BC |
| SMP upgrade includes one 6/667-CPU with 8-MB cache and Tru64 UNIX SMP license | KN311-BB |
| SMP upgrade includes one 6/667-CPU with 8-MB cache and OpenVMS SMP license | KN311-BC |
| Step 4 ( Memory ( Optional |
| System includes one memory option; up to three additional memory options can be added |
| 256-MB memory option (4 x 64 MB DIMMs) | MS340-CA |
| 512-MB memory option (4 x 128 MB DIMMs) | MS340-DA |
| 1-GB memory option (4 x 256 MB DIMMs) | MS340-EA |
| Step 5 ( Additional Power Supplies ( Optional |
| Two 375 watt power supplies included with system; optional third power supply provides N+1 redundancy |
| DS20E redundant power supply | FR-H7910-AA |
| Step 6( Internal Removable Storage ( Optional |
| System supports three internal removable media devices: One combo 24X CD-ROM drive and 1.44 MB disk drive One additional removable media slot provides support for one 5.25( half-height device; Requires KZPBA-CA or KZPCM-DA UltraSCSI adapter, or 3X-KZPCA-AA Ultra2 (LVD) adapter, and SCSI cable (3X-BC56C-2F). For optimum performance it is recommended that Ultra2 capable devices be connected to an Ultra2 adapter |
| 600-MB 32X CD-ROM drive (RRD47) 5.25( half-height, top gun blue | RRD47-VD |
| 12/24-GB 4 mm DAT SCSI tape drive (TLZ10) 5.25( half-height, top gun blue | TLZ10-LB |
| 5.25” half-height 20/40-GB 4 mm DAT Ultra 2 (LVD) SCSI tape drive, top gun blue | 3X-SD20X-LB |
| 5.25” half-height 35/70-GB 8 mm AIT Wide Ultra SCSI tape drive, top gun Blue | 3X-SZ35X-LB |
| 5.25” half-height 50/100-GB 8 mm AIT Ultra 2 (LVD) SCSI tape drive, top gun blue | 3X-SZ50X-LB |
| SCSI cable with one connector and active terminator to connect optional PCI adapter to 5.25( device | 3X-BC56C-2F |
| Step 7 ( M-series Cabinets ( Optional |
| M-series enclosures require selection of the following items: |
| H9A10 or H9A15 cabinet, 120V or 240V |
| Rack kit for each system |
| H9A10 or H9A15 rear cabinet extender |
| Cabinet front door based on cabinet height |
| Factory integration |
| Ballast kit if one or two systems are ordered for the H9A15 cabinet |
| Power Cord |
| Note: For more information on M-Series Cabinet Enclosures, see www.digital.com/alphaserver/products/m-series/index.html |
| Cabinet Configuration Chart for AlphaServer DS20E (5U) with StorageWorks Shelves (4U) |
| Cabinet | Rack Kit | Cabinet Height/Space | Systems | Shelves EV6 EV67 | Ballast Kit |
| H9A10-MC/MD | 3X-BA56R-RA / RC | 56” / 32U | 1 | 6 6 | - |
|  |  |  | 2 | 6 6 | - |
|  |  |  | 3 | 6 6 | - |
|  |  |  | 4 | 4 6 | - |
|  |  |  | 5 | 0 2 | - |
|  |  |  | 6 (EV67 667 MHz only) | 0 0 |  |
| H9A15-MC/MD | 3X-BA56R-RA / RC | 66.5” / 39U | 1 | 6 6 | 1 |
|  |  |  | 2 | 6 6 | 1 |
|  |  |  | 3 | 6 6 | - |
|  |  |  | 4 | 6 6 | - |
|  |  |  | 5 | 4 6 | - |
|  |  |  | 6 | 0 4 | - |
| Note: 1.75” or 1U space is required between each system unit for EV6 500 MHz systems |
| Cabinet Configuration Chart for AlphaServer DS20E (5U) with StorageWorks RA3000 and Disk Shelves (12U) |
| 12U of vertical cabinet space is reserved for one RA3000 controller shelf and up to five disk shelves mounted in top of cabinet, front to back; an additional 2U of vertical space is required for RA3000 controller shelf UPS. |
| Disk shelves can be a combination of RA3000 DS-SWXRA-GN disk shelves and StorageWorks BA36R-RC/RD disk shelves. |
| RA3000 controller shelf supports a maximum of four DS-SWXRA-GN disk shelves; third and fourth DS-SWXRA-GN disk shelf ordered will be installed in rear of M-series cabinet; rear mounted shelves require that a 2-m SCSI cable (BN37A-02) be ordered separately. |
| Systems are supported in remaining vertical space. |
| 1.75( or 1U space is required between each system unit for EV6 500 MHz systems |
| Cabinet | Mounting Kit | Cabinet Height / Space | Systems | RA3000 + Shelves | Ballast Kit |
| H9A10-MC/MD | 3X-BA56R-RA / RC | 54.2( / 32U | 1 | 1 + 5 | - |
|  |  |  | 2 | 1 + 5 | - |
|  |  |  | 3 | 1 + 5 | - |
| H9A15-MC/MD | 3X-BA56R-RA / RC | 66.5( / 39U | 1 | 1 + 5 | 1 |
|  |  |  | 2 | 1 + 5 | 1 |
|  |  |  | 3 | 1 + 5 | - |
|  |  |  | 4 | 1 + 5 | - |
| Cabinet Configuration Chart for AlphaServer DS20E (5U) with StorageWorks BA370 (20U) and Disk Shelves |
| 20U of vertical cabinet space is reserved for one front-mounted BA370 rackmount enclosure, or one front-mounted and one rear-mounted BA370 enclosure in top of cabinet, front to back. Note that top fan (1U) is removed from cabinet when BA370 rackmount enclosure is installed. |
| Systems and StorageWorks shelves are supported in remaining vertical space; StorageWorks shelves are not supported in rear of cabinet behind a front-mounted BA370 rackmount enclosure. |
| 1.75( or 1U space is required between each system unit. |
| Cabinet | Rack Kit | Cabinet Height/Space | Systems | BA370 | Shelves |
| H9A10-MC/MD | 3X-BA56R-RA / RC |  | 1 | 1 (front) or | 2 |
|  |  |  | 2 | 2 (front & back) | 0 |
| H9A15-MC/MD | 3X-BA56R-RA / RC | 66.5” / 40U | 1 | 1 (front) or | 6 |
|  |  |  | 2 | 2 (front & back) | 4 |
|  |  |  | 3 |  | 0 |
| Note: Installing one BA370 and one system in an H9A15 cabinet requires the mandatory selection of a ballast kit; a ballast kit is not required if two BA370s and one system are installed in H9A15 cabinet. |
| M-series Cabinets |
| 67" cabinet with 56" or 32U of usable vertical space, 120V dual-24A controller, each with 10 NEMA 5-15R outlets, input power plug NEMA L5-30P, Americas, Asia Pacific; includes rear door and top fan tray | H9A10-MC |
| 67" cabinet with 56" or 32U of usable vertical space, 240V dual-16A controller, each with 12 IEC C13 outlets, input power plug IEC 309, 16A, Europe; includes rear door and top fan tray | H9A10-MD |
| 79" cabinet with 66.5" or 39U of usable vertical space, 120V dual-24A controller, each with 10 NEMA 5-15R outlets, input power plug NEMA L5-30P, Americas, Asia Pacific; includes rear door and top fan tray | H9A15-MC |
| 79" cabinet with 66.5" or 39U of usable vertical space, 240V dual-16A controller, each with 12 IEC C13 outlets, input power plug IEC 309, 16A, Europe; includes rear door and top fan tray | H9A15-MD |
| Rear Cabinet Extender ( Required selection of one cabinet extender for each H9A10 or H9A15 cabinet |
| Rear cabinet extender, top gun blue, for H9A10-MC/MD cabinets | H9C10-TE |
| Rear cabinet extender, top gun blue, for H9A15-MC/MD cabinets | H9C15-TE |
| Cabinet Front Door ( Required selection of door based on cabinet height |
| Front door, top gun blue, for H9A10-MC/MD cabinet enclosure | H9C10-TF |
| Front door, top gun blue, for H9A15-MC/MD cabinet enclosure | H9C15-TF |
| Factory Integration ( Required |
| Factory Integration of systems and storage devices assembled and configured in cabinet enclosure in predefined locations | YS-ASCAA-AA |
| Ballast Kit ( Required only if one system is ordered for the H9A15 cabinet |
| Ballast is added to a cabinet at particular locations for specific configurations to meet safety regulations for installation, operation, and service; see Cabinet Configuration Chart |
| Two 35-40 lb. Steel plates | H9C10-MC |
| Rackmount Power Cord ( Required for each system |
| US/Canada | BN20Z-4E |
| Non-US | BN35S-4E |
| Japan, 2.5m | 3X-BN46D-4E |
| Shelves Supported in M-series Cabinets ( Optional |
| UltraSCSI single-ended RETMA rack, single-bus personality module, 180W power supply | BA36R-RC |
| UltraSCSI single-ended RETMA rack, split-bus personality module, 180W power supply | BA36R-RD |
| 180W power supply, includes 120V North American and 240V IEC power cord | CK-BA35X-HH |
| Compaq CustomSystems Support |
| Cabinets containing systems and storage must be assembled by qualified assemblers: Compaq Manufacturing, Compaq CustomSystems, or an authorized Compaq Certified Integration Partner. For custom integration of systems, options, cabinet expansion offerings, and additional Compaq and third party devices, or for other cabinets, doors, and trim kits of a different color, contact Compaq CustomSystems at 1-800-AT COMPAQ, or your local authorized Compaq Certified Integration Partner. |
| Step 8 (External Storage ( Optional |
| UltraSCSI Configuration Rules |
| UltraSCSI configurations require UltraSCSI components (controllers, adapters, shelves, disks, and cables) |
| UltraSCSI adapters and RAID controllers support UltraSCSI disks at UltraSCSI speeds in UltraSCSI top gun blue shelves (DS-BA356-xx) |
| UltraSCSI StorageWorks Pedestals |
| UltraSCSI top gun blue pedestals provide support for UltraSCSI disk drives; pedestal is available in single-bus or split-bus configurations and includes a personality module and 180W power supply |
| UltraSCSI shelf supports: seven 3.5( hard disk drives, or one 5.25( device and four 3.5( hard disk drives, or two 5.25( devices and one 3.5( hard disk drive |
| Installation of redundant power supply reduces number of 3.5( drive slots by one |
| UltraSCSI single-ended pedestal, single-bus personality module, 180W power supply | DS-BA356-KF |
| UltraSCSI single-ended pedestal, split-bus personality module, 180W power supply | DS-BA356-KG |
| UltraSCSI pedestal, single-channel differential personality module, 180W power supply | DS-BA356-KH |
| 180W power supply, includes 120V North American and 240V IEC power cord | CK-BA35X-HH |
| Tabletop Tape Drives |
| Tape drives require UltraSCSI adapter and country-specific power cord |
| 12/24-GB 4-mm DAT narrow single-ended tabletop SCSI tape, includes 120V North American power cord, requires BN31W-xx SCSI cable | DS-TLZ10-DB |
| 35/70-GB DLT single-ended tabletop tape drive, requires BN21K-xx SCSI cable | DS-TZ89N-TA |
| 50/100-GB US AIT tabletop tape drive (includes SCSI cable and power cord) | 157767-001 |
| 50/100-GB International AIT tabletop tape drive (includes SCSI cable and power cord) | 157767-B31 |
| 50/100-GB Japan AIT tabletop tape drive (includes SCSI cable and power cord) | 157767-291 |
| Storage Controllers/Adapters for External StorageWorks Shelves |
| Storage controllers require Tru64 UNIX V4.0F or OpenVMS V7.1-2 |
| Note: The following controllers are only supported with StorageWorks shelves (not supported with the 3X-BA611-4D disk drive cage) |
|  | Maximum # Supported |  |
|  | Tru64 UNIX | OpenVMS |  |
| PCI Fibre Channel adapter (KGPSA-BC), (uses one slot) | 4 | 4 | 380574-001 |
| Fibre Channel cable (BNGBX-xx) xx=02, 05, 15, 30, 50 meters x=1, 2, 3, 4, 5 |  | 234457-B2x |
| PCI 2-port UltraSCSI single-ended adapter and 10/100 Mb Ethernet combo adapter (uses one PCI slot); includes internal 68-pin and 50-pin HD connectors and two external 68-pin VHDCI SCSI connectors, requires BN37A-xx cable to connect to single-ended UltraSCSI shelf | 4 | 4 | KZPCM-DA |
| VHDCI male-to-VHDCI male UltraSCSI cable, xx = 02, 2E [2.5], 03, 05, 10, 20 m |  | BN37A-xx |
| PCI 1-port UltraSCSI single-ended adapter (uses one PCI slot); includes internal 68-pin and 50-pin HD connectors and external 68-pin HD connector, requires BN38C-xx cable (2 to 20 m) to connect to single-ended UltraSCSI shelf | 4 | 4 | KZPBA-CA |
| PCI 1-port UltraSCSI differential adapter (uses one PCI slot); includes external 68-pin HD connector, requires BN38C-xx cable (2 to 25 m) to connect adapter to differential UltraSCSI shelf or RAID controller | 4 | 4 | KZPBA-CB |
| 68-pin HD male-to-VHDCI male UltraSCSI cable; xx = 02, 03, 05, 10, 20, 25 m |  | BN38C-xx |
| PCI 1-port UltraSCSI RAID controller with 4-MB cache memory (uses one PCI slot), includes RAID Array 230/Plus Subsystem software and documentation kit; includes VHDCI female connector; tape drives not supported; 18.2-GB disk drives not supported, requires BN37A-xx cable (.3 to 20 m) to connect to single-ended UltraSCSI shelf | 4 | 4 | KZPAC-AA |
| PCI 3-port UltraSCSI RAID controller with 4-MB cache memory (uses one PCI slot), includes RAID Array 230/Plus Subsystem Software and documentation kit; tape drives not supported; 18.2-GB disk drives not supported; SCSI cable required for each active port; requires BN37X-xx cable (.3 to 20 m) to connect to single-ended UltraSCSI shelf, and BN31K-0E for external third port connection | 2 | 2 | KZPAC-CA |
| Same as KZPAC-CA with 8-MB cache memory | 2 | 2 | KZPAC-CB |
| Cache battery backup for KZPAC controller |  | KZPSC-UB |
| Factory configured RAID of KZPAC with StorageWorks shelves Note: Factory configured RAID sets for disks in single-bus StorageWorks shelves connected to KZPAC require completion of questionnaire located at http://www.digital.com/alphaserver/fcr |  | YS-ASDRD-BA |
| VHDCI male-to-VHDCI male UltraSCSI cable; xx = 02, 2E [2.5], 03, 05, 10, 20, 25 m Note: Manufacturing may substitute BN37A-02 cable for specific cabinet configurations. |  | BN37A-xx |
| SCSI cable/bulkhead assembly kit, supports one third-port connection from KZPAC-CA/CB, allows external connection of one third port |  | BN31K-0E |
| SCSI cable/bulkhead assembly kit, supports two third-port connections from KZPAC-CA/CB, allows external connection of two third ports |  | KZPAC-SB |
| Removable Media Devices for External StorageWorks Shelves |
| For maximum performance, tape libraries must be configured with Fast Wide Differential (FWD) controllers for tape backup |
| 12/24-GB 4 mm DAT narrow SCSI tape drive in StorageWorks carrier | DS-TLZ10-VA |
| 35/70-GB DLT single-ended tape drive in StorageWorks carrier | DS-TZ89N-VW |
| 35/70-GB AIT tape drive in StorageWorks carrier | DS-AIT35-VW |
| 600-MB 32X CD-ROM drive in StorageWorks carrier | DS-RRD47-VA |
| BA370 Rackmount Enclosure |
| Mandatory rear cabinet extender ordered for systems installed in M-series cabinets (H9A10 and H9A15) allows two BA370 enclosures to be installed front to back in cabinet. |
| Host adapter, RAID Array controller, cache battery, platform specific Solutions Software Kit, and disk drives must be ordered separately. |
| BA370 front mount rackmount enclosure with five 180W power supplies, includes RETMA rackmount kit; first BA370 enclosure must be front mounted in cabinet, 20U height | 2T-BA370-AS |
| BA370 rear mount rackmount enclosure with five 180W power supplies, includes RETMA rackmount kit; second BA370 enclosure must be rear mounted in cabinet, 20U height | 2T-BA370-AR |
| Factory configured RAID of rackmounted BA370/HSZ70 | YS-ASCRD-AA |
| Note: Factory configured RAID sets for disks in rackmounted BA370 StorageWorks shelf controlled by one or two HSZ70s require completion of questionnaire located at http://www.digital.com/alphaserver/fcr |
| StorageWorks Shelf ( Requires selection of UltraSCSI adapter and SCSI cable |
| StorageWorks UltraSCSI single-bus shelf kit | BA36R-RC |
| StorageWorks UltraSCSI split-bus shelf kit | BA36R-RD |
| External Disk Drive (Supported in StorageWorks Shelf) |
| 9.1-GB 7200 RPM UltraSCSI drive | DS-RZ1DA-VW |
| 18.2-GB 7200 RPM UltraSCSI drive | DS-RZ1EA-VW |
| 36.4-GB 7200 RPM UltraSCSI drive | DS-RZ1FB-VW |
| 9.1-GB 10000 RPM UltraSCSI drive | DS-RZ1DD-VW |
| 18.2-GB 10000 RPM UltraSCSI drive | DS-RZ1ED-VW |
| 36.4-GB 10,000 rpm UltraSCSI drive | DS-RZ1FC-VW |
| Note- A maximum of (6) 18.2-GB and 36.4 GB 10000 RPM drives can be configured in a Storageworks shelf |
| Step 9 (UltraSCSI RAID Array Controllers and UltraSCSI RAID Packaged Solutions (Optional |
| RAID Array 3000 Rackmount Controller Shelf |
| Selection of RA3000 Solutions Software Kit is required |
| Supported SCSI adapter: KZPBA-CB PCI 1-port UltraSCSI differential adapter |
| RA3000 rackmount controller shelf, blue, with one controller, 110V Includes: UltraSCSI BA356 controller shelf, one HSZ22 2-channel controller with 16-MB cache, integrated Environmental Monitoring Unit (EMU), two 180W power supplies, two dual-port host differential UltraSCSI I/O SBBs, dual-channel UltraSCSI single-ended personality modules, one 120V 1000VA rackmount UPS, 5-m host SCSI cable (BN37A-05), BN38E-0B adapter, UPS serial cable, PC connection serial cable (DB-9), two 68-pin HD tri-link adapters (H8861-AA), two North American power cords, and RETMA mounting bracket (disk shelves and disks not included) Requires: Solutions Software Kit for platform, host adapter, RA3000 disk shelf, and disks Options: Second HSZ22 controller, up to four additional RA3000 disk shelves, cache memory upgrade | DS-SWXRA-GH |
| RA3000 rackmount controller shelf, blue, with one controller, 230V Includes: UltraSCSI BA356 controller shelf, one HSZ22 2-channel controller with 16-MB cache, integrated Environmental Monitoring Unit (EMU), two 180W power supplies, two dual-port host differential UltraSCSI I/O SBBs, dual-channel UltraSCSI single-ended personality modules, one 230V 1000VA rackmount UPS, 5-m host SCSI cable (BN37A-05), BN38E-0B adapter, UPS serial cable, PC connection serial cable (DB-9), two 68-pin HD tri-link adapters (H8861-AA), RETMA mounting bracket (disk shelves and disks not included) Requires: Solutions Software Kit for platform, two country-specific power cords, host adapter, RA3000 disk shelf, and disks Options: Second HSZ22 controller, up to four additional RA3000 disk shelves, cache memory upgrade | DS-SWXRA-GK |
| RAID Array 3000 Rackmount Disk Shelf |
| Select one to four disk shelves |
| Third and fourth DS-SWXRA-GN disk shelf ordered will be installed in rear of M-series cabinet; rear mounted shelves require that a 2-m BN37A-02 SCSI cable be ordered |
| RA3000 rackmount disk shelf, blue, includes UltraSCSI BA356 disk shelf, two 180 W power supplies, single-ended UltraSCSI personality card, one half meter SCSI cable (BN37A-0E), two North American power cords, and RETMA mounting bracket (disks not included); order two country-specific power cords for non-North American use | DS-SWXRA-GN |
| HSZ22 Controller |
| Note that second HSZ22 controller ordered is field installed only, not factory installed; requires BN37A-0E SCSI jumper cable be ordered separately |
| Second HSZ22 controller with 16-MB cache and two 16-MB SIMMs for mirror cache, one BN37A-05 5-m UltraSCSI cable, one BN38E-0B cable adapter ( field installable only; note that second HSZ22 controller does not require additional Solution Software Kit | DS-HSZ22-AA |
| Second HSZ22 controller with 32-MB cache and two 32-MB SIMMs for mirror cache, one BN37A-05 5-m UltraSCSI cable, one BN38E-0B cable adapter ( field installed only; note that second HSZ22 controller does not require additional Solution Software Kit | DS-HSZ22-AB |
| RA3000 Solutions Software Kit |
| StorageWorks Command Console (SWCC) software |
| Platform specific software |
| Installation scripts and installation documentation |
| RA3000 Solutions Software Kit for Tru64 UNIX | QB-5TWAB-SA |
| RA3000 Solutions Software Kit for OpenVMS | QB-5TWAC-SA |
| HSG80/HSZ80 External Controllers |
| Fibre Channel controller (DS-HSG80-BJ), includes 2-MB cache expandable to 128 MB; requires 128697-B21 HSG80 ACS V8.4F software kit or 128698-B21 V8.4P software kit for each HSG80 ordered; | 380672-B21 |
| Fibre Channel controller (DS-HSG80-BH), includes 64-MB cache expandable to 128 MB; requires 128697-B21 HSG80 ACS V8.4F software kit or 128698-B21 V8.4P software kit for each HSG80 ordered; | 380671-B21 |
| UltraSCSI controller (DS-HSZ80-AH), includes 64-MB cache expandable to 128 MB; requires 400569-001 for Tru64 UNIX or 400571-001 for OpenVMS | 400564-B21 |
| UltraSCSI controller (DS-HSZ80-AJ), includes 256-MB cache expandable to 512 MB; requires 400569-001 for Tru64 UNIX or 400571-001 for OpenVMS | 400565-B21 |
| ESA 10000 , RAID Array 7000, RAID Array 8000 |
| Enterprise Storage Array 10000 and RAID Array 7000 (HSZ70) product set are supported on AlphaServer DS20E systems |
| Supported SCSI adapter for HSZ80/HSZ70 ( KZPBA-CB PCI 1-port UltraSCSI differential adapter |
| Supported SCSI adapter for HSG80 ( KGPSA-BC PCI 1-port Fiber-Channel adapter |
| Step 10 (Graphics Adapters (Optional |
| RAID Configuration Utility is accessible via console port for Tru64 UNIX and OpenVMS systems; optional graphics capability available |
| Select graphics adapter, monitor, and country-specific keyboard if required |
|  | Maximum # Supported |  |
|  | Tru64 UNIX | OpenVMS |  |
| ELSA Gloria synergy graphics with 8-MB SGRAM 1600 x 1200, 2D/3D graphics accelerator | 3 | 1 | SN-PBXGK-BB |
| PowerStorm 4D51T advanced 3D graphics accelerator | 4 | - | SN-PBXGI-AD |
| PowerStorm 300 3D multi-head graphics accelerator with 15-MB frame buffer memory and 16-MB texture memory | 3 | - | SN-PBXGD-AD |
| PowerStorm 350 3D multi-head graphics accelerator with 30-MB frame buffer memory and 32-MB texture memory | 3 | - | SN-PBXGD-AE |
| Step 11 (Monitors (Optional |
| RAID Configuration Utility is accessible via the console port for Tru64 UNIX and OpenVMS systems; optional graphics capability is available |
| Graphics monitors other than those listed can be used if compatible with SVGA graphics ordered with system |
| Selection of a video extension cable and country-specific power cord is mandatory for all monitors |
| 15( Corporate Series auto-scan color monitor, VGA to 1024 x 768 @ 85 Hz; Northern Hemisphere without power cord | 3R-VRQV5-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQV5-11 |
| 17( (16.0( viewable image size) professional series auto-scanning color monitor, Trinitron CRT, 0.25 mm aperture grill pitch, VGA to 1280 x 1024 @75 Hz, TCO 99, MPR-II, Energy Star, attached 1.8-m video cable; Northern Hemisphere without power cord | 3R-VRQP7-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQP7-23 |
| 21( (19.6( viewable image size) auto-scanning color monitor, Trinitron CRT, 0.28 mm aperture grill pitch, VGA to 1600 x 1200 @85 Hz NI, TCO 95, Energy Star, includes 1.8-m video cable; Northern Hemisphere without power cord | 3R-VRQP1-24 |
| Same as above except Southern Hemisphere without power cord | 3R-VRQP1-23 |

| Video Extension Cable |
| --- |
| 1.8-m video extension cable—mandatory for each monitor ordered | BN39C-02 |
| Monitor Power Cords |
| North American, 120V, 75( | BN26J-1K |
| Australia, New Zealand, 2.5m | BN19H-2E |
| Central Europe, 2.5m | BN19C-2E |
| UK, Ireland, 2.5m | BN19A-2E |
| UK, Ireland, 2.5m | BN19A-2E |
| Switzerland, 2.5m | BN19E-2E |
| Denmark, 2.5m | BN19K-2E |
| Italy, 2.5m | BN19M-2E |
| Egypt, India, South Africa, 2.5m | BN19S-2E |
| Israel, 2.5m | BN18L-2E |
| Japan, 2.5m | 3X-BN46F-02 |
| Step 12 (Networks and Communications ( Optional |
| Controllers/adapters require Tru64 UNIX V4.0F or OpenVMS V7.1-2 |
| See Step 2 for mandatory supported Ethernet adapters |
|  | Maximum # Supported |  |
|  | Tru64 UNIX | OpenVMS |  |
| FE FX Daughtercard for 3X-DE602-AA (3X-DE602-AA is a prerequisite) | 2 | 2 | 3X-DE602-FA |
| PCI Gigabit Ethernet adapter, SC connectors, MMF, no boot support | 2 | 1 | DEGPA-SA |
| SC-to-SC dual fiber optic cable |  | BN34B-xx |
| PCI FDDI adapter, single attachment station (SAS), multi-mode fiber (MMF), SC connector | 2 | 2 | 3X-DEFPA-AC |
| PCI FDDI adapter, DAS, MMF, SC connector | 2 | 2 | 3X-DEFPA-DC |
| MIC-SC dual fiber optic cable |  | BN34D-xx |
| SC-to-SC dual fiber optic cable |  | BN34B-xx |
| PCI FDDI adapter, SAS, TP-PMD, requires BN25H-03 cable | 2 | 2 | 3X-DEFPA-UC |
| PCI FDDI dual adapter, DAS, TP-PMD, requires BN25H-03 cable | 2 | 2 | 3X-DEFPA-MC |
| 3m (9.8") FDDI cross-over cable |  | BN25H-03 |
| PCI 4-port asynchronous controller | 2 | 2 | PBXDA-AA |
| PCI 8-port asynchronous controller, cable included | 2 | 2 | PBXDA-AB |
| PCI 16-port asynchronous controller, cable included | 2 | 2 | PBXDA-AC |
| PCI-to-ATM 155 Mb adapter - Fiber | 4 | - | 3X-DAPBA-FA |
| PCI-to-ATM 155 Mb adapter - UTP | 4 | - | 3X-DAPBA-UA |
| PCI-to-ATM 622 Mb adapter - Fiber | 2 | - | 3X-DAPCA-FA |
| Asynchronous multi-port MUX expander XEM |  | CXI01-AB |
| Step 13 ( MEMORY CHANNEL (Optional |
| Tru64 UNIX Systems |
| Requires a minimum of Tru64 UNIX V4.0F with TruCluster V1.6 or later |
| Each system node in the cluster requires a TruCluster Production Server (QB-3RLAE-KA) or TruCluster MEMORY CHANNEL software license (QB-4ZCAE-AA) |
| TruCluster MEMORY CHANNEL license (QB-4ZCAG-AA), normally used for high performance technical computing applications, not required if systems have a TruCluster Production Server license (QB-3RLAE-KA) |
| OpenVMS Systems |
| Requires OpenVMS V7.1-2 or later and OpenVMS Cluster license (QL-MUZAE-AA) |
| Configuring Information |
| Up to two PCI to System Area Network adapters (CCMAB-AA) are supported in a single system |
| Two-node clusters can be configured by ordering a CCMAB-AA for each system and one BN29B-04 or BN29B-10 cable; the cable connects directly to the CCMAB-AA in each system |
| For three or four system nodes, order one CCMAB-AA adapter, one BN29B-04 or BN29B-10 cable and one CCMHB-AA; make connections from the CCMAB-AA in a system to the CCMHB-AA |
| CCMHB-AA includes four CCMLB-AA line cards and supports up to four nodes; expansion up to eight system nodes can be achieved by adding up to four additional CCMLB-AA line cards |
| If two CCMAB-AA’s are configured in each system, a second CCMHB-AA is required for three or more nodes; in two-node clusters, the CCMAB-AA’s may be directly connected |
| MEMORY CHANNEL Controller |
| PCI System Area Network Controller, maximum two | CCMAB-AA |
| System Area Network Hub with four line cards; includes BN19P-2E power cord for Canada, Japan, and US operations(for other regions, order appropriate power cord from list below | CCMHB-AA |
| Expansion line card for CCMHB hub | CCMLB-AA |
| 4-m cable for CCMAB and CCMHB | BN39B-04 |
| 10-m cable for CCMAB and CCMHB | BN39B-10 |
| TruCluster Production Server Software for Tru64 UNIX | QB-3RLAE-AA |
| Tru64 UNIX Driver for MEMORY CHANNEL license | QB-4ZCAE-AA |
| OpenVMS Cluster license for Alpha systems | QL-MUZAE-AA |
| MEMORY CHANNEL Power Cords |
| Ireland, United Kingdom | BN19A-2E |
| Egypt, India | BN19S-2E |
| Central Europe | BN19C-2E |
| Israel | BN18L-2E |
| Switzerland | BN19E-2E |
| Italy | BN19M-2E |
| Denmark | BN19K-2E |
| Australia, New Zealand | BN19H-2E |
| Step 14 (Keyboards |
| Keyboards are not included with system and must be ordered separately |
|  | Tru64 UNIX | OpenVMS |
| U.S./English keyboard | SN-LKQ47-AA | LK461-A2 |
| Belgian keyboard | SN-LKQ47-AB | LK461-AB |
| Canadian/French keyboard | SN-LKQ47-AC | LK461-AC |
| Danish keyboard | SN-LKQ47-AD | LK461-AD |
| UK keyboard | SN-LKQ47-AE | - |
| Finnish keyboard | SN-LKQ47-AF | LK461-AF |
| German keyboard | SN-LKQ47-AG | LK461-AG |
| Dutch keyboard | SN-LKQ47-AH | LK461-AH |
| Italian keyboard | SN-LKQ47-AI | LK461-AI |
| Swiss/French keyboard | SN-LKQ47-AK | LK461-AK |
| Swiss/German keyboard | - | LK461-AL |
| Swedish keyboard | SN-LKQ47-AM | LK461-AM |
| Norwegian keyboard | SN-LKQ47-AN | LK461-AN |
| French keyboard | SN-LKQ47-AP | LK461-AP |
| Canadian/English keyboard | - | LK461-AQ |
| Latin-American keyboard | SN-LKQ47-AR | - |
| Spanish keyboard | SN-LKQ47-AS | LK461-AS |
| Hebrew keyboard | SN-LKQ47-AT | LK461-AT |
| Portuguese keyboard | SN-LKQ47-AV | LK461-AV |
| BHCSY keyboard | SN-LKQ47-AX | - |
| International keyboard | SN-LKQ47-BA | - |
| Greek keyboard | SN-LKQ47-BH | LK461-BH |
| Taiwanese keyboard | SN-LKQ47-BI | - |
| Korean keyboard | SN-LKQ47-BK | - |
| Romanian keyboard | - | LK461-BL |
| Polish keyboard | SN-LKQ47-BP | LK461-BP |
| Hungarian keyboard | SN-LKQ47-BQ | LK461-BQ |
| Arabic keyboard | SN-LKQ47-BR | - |
| Cyrillic keyboard | SN-LKQ47-BT | LK461-BT |
| Turkish keyboard | SN-LKQ47-BU | LK461-BU |
| Czech keyboard | SN-LKQ47-BV | LK461-BV |
| Turkish/French keyboard | - | LK461-BW |
| Yugoslavian keyboard | - | LK461-BY |
| Thai keyboard | SN-LKQ47-CB | - |
| S. Chinese keyboard | SN-LKQ47-CV | - |
| Slovak keyboard | SN-LKQ47-CZ | LK461-CZ |
| Keyboard or Mouse Extension Cable |
| 6 ft keyboard or mouse extension cable; to extend both keyboard and mouse order 2 cables | 17-04016-01 |
| Step 15 (Console Terminal ( Optional |
| Any terminal can be used as a console device |
| Third-party console devices require an EIA-232 25-pin DSUB connector |
| VT510 video terminal; requires H857-x cable | VT510-xx |
| Console cable, female connector | H857-A |
| Console cable, male connector | H857-D |
| Console cable, male connector (IBM compatible) | H897-E |
| Step 16 ( Software ( Required selection of media and documentation for first system on site |
| Software Processor Code = E |
| Tru64 UNIX |
| Tru64 UNIX systems include Tru64 UNIX Traditional Unlimited User license, Server Extension, Internet Access Software kit, and Netscape's Enterprise Server 3.0 |
| Tru64 UNIX media and online documentation on CD-ROM | QA-MT4AA-H8 |
| Tru64 UNIX full hard copy documentation | QA-MT4AA-GZ |
| StorageWorks Software Package, includes licenses for Logical Storage Manager and AdvFS Utilities | QB-5RXAE-AA |
| TruCluster Available Server License | QL-05SAE-AA |
| Advanced Server for Tru64 UNIX, 25 client concurrent use license | QL-5U29M-3D |
| Advanced Server for Tru64 UNIX, 50 client concurrent use license | QL-5U29M-3E |
| Advanced Server for Tru64 UNIX, 100 client concurrent use license | QL-5U29M-3F |
| Advanced Server for Tru64 UNIX, 250 client concurrent use license | QL-5U29M-3G |
| Advanced Server for Tru64 UNIX, 500 client concurrent use license | QL-5U29M-3H |
| Layered products media and documentation for Tru64 UNIX on CD-ROM | QA-054AA-H8 |
| DECnet/OSI end-system license for Tru64 UNIX | QL-MTJAE-AA |
| DECnet/OSI extended function license for Tru64 UNIX | QL-MTKAE-AA |
| OpenVMS |
| OpenVMS systems include OpenVMS base license and Enterprise Integration Package V2.0 |
| OpenVMS Concurrent Use Licenses are not specific to a single system and can be moved between systems at user discretion; OpenVMS Concurrent Use Licenses can also be shared in a mixed OpenVMS VAX and OpenVMS Alpha Cluster |
| Concurrent Use 1-user license | QL-MT3AA-3B |
| Concurrent Use 2-user license | QL-MT3AA-3C |
| Concurrent Use 4-user license | QL-MT3AA-3D |
| Concurrent Use 8-user license | QL-MT3AA-3E |
| Concurrent Use 16-user license | QL-MT3AA-3F |
| Concurrent Use 32-user license | QL-MT3AA-3G |
| Concurrent Use 64-user license | QL-MT3AA-3H |
| Concurrent Use 128-user license | QL-MT3AA-3J |
| Concurrent Use 256-user license | QL-MT3AA-3K |
| Traditional unlimited user license | QL-MT2AQ-AA |
| OpenVMS media and documentation on CD-ROM | QA-MT1AA-H8 |
| OpenVMS full hard copy documentation | QA-001AA-GZ |
| Layered products media and documentation for OpenVMS on CD-ROM, includes Enterprise Integration Server for OpenVMS media and documentation | QA-03XAA-H8 |
| DIGITAL Enterprise Integration Server for OpenVMS media and documentation | QA-5LVAA-H8 |
| DECnet extended function license for OpenVMS | QL-MTGAE -AA |
| DECnet end-system to extended function upgrade license for OpenVMS | QL-MTHAE-AA |
| OpenVMS Cluster license for Alpha systems | QL-MUZAE-AA |
| OpenVMS Volume Shadowing license | QL-2A1AE-AA |
| Step 17 ( Hardware and Software Supplemental Support Services |
| Systems include 3-year hardware warranty, on-site, with 5 x 9, 24-hour response time; select optional Hardware Supplemental Support Services if required |
| Options ordered as part of "Initial System Sale" take on warranty of the enclosure; options added after "Initial System Sale" take on warranty of enclosure until enclosure warranty ends |
| All unique AlphaServer DS20E options have a minimum of 1-year Return-to-Compaq warranty |
| Hardware Supplemental Support (Americas and Asia Pacific only | 1-GB memory or less | More than 1-GB memory |
| 5 x 9, 4-hour response time | FM-TC4HR-36 | FM-TF4HR-36 |
| 5 x 12, 4-hour response time | FM-TC512-36 | FM-TF512-36 |
| 6 x 16, 4-hour response time | FM-TC616-36 | FM-TF616-36 |
| 7 x 24, 4-hour response time | FM-TC724-36 | FM-TF724-36 |
| Years 1-5, next day, onsite | FM-TCXHW-60 | FM-TFXHW-60 |
| Years 1-5, 5 x 9, 4-hour response time | FM-TC4HR-60 | FM-TF4HR-60 |
| Years 1-5, 5 x 12, 4-hour response time | FM-TC512-60 | FM-TF512-60 |
| Years 1-5, 6 x 16, 4-hour response time | FM-TC616-60 | FM-TF616-60 |
| Years 1-5, 7 x 24, 4-hour response time | FM-TC724-60 | FM-TF724-60 |
| Installation Services |
| Hardware product installation for DS20E | FM-TC12X-IN |
| Add-on memory installation for DS20E | FM-TCMEM-IN |
| Add-on CPU installation for DS20E | FM-TCSMP-IN |
| Software Supplemental Support— Americas and Asia Pacific only |
| Systems include 90-day Conformance to SPD and Telephone Advisory Support; select optional Software Supplemental Support Services if required |
| Software service upgrades for Tru64 UNIX include advisory and remedial software support with new version license rights for operating system for time period indicated |
| Software service upgrades for OpenVMS include advisory and remedial software support with new version license rights for operating system and Enterprise Integration Package for time period indicated |
| Software service upgrades for SMP upgrades running Tru64 UNIX or OpenVMS include new version license rights for Tru64 UNIX or OpenVMS SMP Upgrades for time period indicated; one required for each SMP upgrade |
|  | Tru64 UNIX | OpenVMS |
| 5X9 12-month Software Supplemental Support | FM-D20U9-12 | FM-D20V9-12 |
| 5X9 36-month Software Supplemental Support | FM-D20U9–36 | FM-D20V9-36 |
| 5X9 60-month Software Supplemental Support | FM-D20U9-60 | FM- D20V9-60 |
| 7X24 12-month Software Supplemental Support | FM-D20US-12 | FM-D20VS-12 |
| 7X24 36-month Software Supplemental Support | FM-D20US–36 | FM- D20VS-36 |
| 7X24 60-month Software Supplemental Support | FM-D20US-60 | FM- D20VS-60 |
| 12-month Software Supplemental Support ( DS20E SMP Upgrade | FM-D20UP-12 | FM-D20VP-12 |
| 36-month Software Supplemental Support ( DS20E SMP Upgrade | FM-D20UP-36 | FM-D20VP-36 |
| 60-month Software Supplemental Support( DS20E SMP Upgrade | FM-D20UP-60 | FM-D20VP-60 |

| Pedestal |  | Dimensions (HxWxD) | 18.5 x 8.85 x 27.5 in / 47.0 x 22.5 x 69.9 cm |
| --- | --- | --- | --- |
|  |  | Shipping Dimensions | 24 x 26.25 x 40 in / 61.0 x 66.0 x 101.6 cm |
|  |  | Weight |  |
|  |  | Typical Configuration | 80 lbs/36 kg |
|  |  | Maximum Configuration | 88 lbs/ 40 kg |
|  |  | Shipping Weight |  |
|  |  | Nominal | 100 lbs/ 45 kg |
|  |  | Maximum | 110 lbs/ 50 kg |
|  |  | Clearances | Operating | Service |
|  |  | Front | 15 in/ 38.1 cm | 15 in/ 38.1 cm |
|  |  | Rear | 6 in/15 cm | 29.5 in/75 cm |
|  |  | Left Side | None | None |
|  |  | Right Side | None | None |
| Rackmount |  | Dimensions (HxWxD) | 8.75 x 17.5 x 26 in/22.2 x 44.5 x 66.0 cm (5U) |
|  |  | Shipping Dimensions | 24 x 26.25 x 40 in/61.0 x 66.0 x 101.6 cm |
|  |  | Weight |  |
|  |  | When lifting: |  |
|  |  | Nominal | 80 lbs/36 kg |
|  |  | Maximum | 86 lbs/39 kg |
|  |  | Total added to cabinet (brackets, slides, cables): |  |
|  |  | Nominal | 84 lbs/38 kg |
|  |  | Maximum | 88 lbs/40 kg |
|  |  | Shipping Weight |  |
|  |  | Nominal | 100 lbs/45 kg |
|  |  | Maximum | 110 lbs/50 kg |
|  |  | Clearances | Operating | Service |
|  |  |  | See specific cabinet requirements | Minimum 4 ft / 121.9 cm, 28 in / 71 cm withdrawal on rails |
| Cabinet |  |  | H9A10 M-Series | H9A15 M-Series |
|  |  | Dimensions (HxWxD) | 67 x 23.6 x 43.27 in/ 170 x 60 x 110 cm | 79 x 23.6 x 35.4 in 200 x 60 x 90 cm |
|  |  | Shipping Dimensions | 73 x 36 x 48 in / 185.5 x 91.5 x 122 cm | 85 x 36 x 48 in / 216 x 91.5 x 122 cm |
|  |  | Weight | Configuration dependent | 1000 lbs / 450 kg |
|  |  | Shipping Weight | Configuration dependent, maximum payload 1,000 lbs | 1056 lbs / 550 kg (normal) 1,408 lbs / 640 kg (maximum) |
| System Unit |  | Environmental |  |
|  |  | Temperature |  |
|  |  | Operating (Tower, Rackmount)1 | 50( to 95(F/10( to 35(C |
|  |  | Non-operating | Not tested |
|  |  | Storage (60 days) | –40( to –151(F/–40 to –66(C |
|  |  | Rate of change | 20(F/hr/11(C/hr |
|  |  | Relative Humidity |  |
|  |  | Operating | 20% to 80% |
|  |  | Non-operating | 20% to 80% |
|  |  | Storage (60 days) | 10% to 95% |
|  |  | Rate of change | 20% hr |
|  |  | Maximum Wet Bulb Temperature |  |
|  |  | Operating | 82(F/28(C |
|  |  | Storage (60 days) | 115(F/46(C |
|  |  | Maximum Dew Point Temperature |  |
|  |  | Operating | 36(F/2(C |
|  |  | Storage (60 days) | Not tested |
|  |  | Heat Dissipation | Nominal | Maximum |
|  |  | Tower | 550W, 1,878 BTU/hr | 780W, 2,664 BTU/hr |
|  |  | Pedestal |  |  |
|  |  | H9A10/H9A15 Cabinets | Configuration dependent |  |
|  |  | Air Flow and Quality |  |
|  |  | Intake location | Front |
|  |  | Exhaust location | Rear Tower, Pedestal, Rack; Rear/top H9A10/H9A15 |
|  |  | Particle size | N/A |
|  |  | Concentration | N/A |
|  |  | Altitude |  |
|  |  | Operating 2 | 10,000 f/3,037m |
|  |  | Non-operating | 40,000 ft/12,192m |
|  |  | Acoustics (Declared values per ISO 9296 and ISO 7779) |
|  |  | Acoustics 3 | LWAd3B | LnAm5dBA (bystander position) |
|  |  | Idle | 5.8 | 44 |
|  |  | Operating | 6.3 | 49 |
|  |  | Vibration |  |
|  |  | Operating | 10-500 Hz .1 G peak |
|  |  | Non-operating | 1.03 Grms 5-300 Hz |
| System Unit (continued) |  | Electrical (Power supplies are universal, PFC, auto ranging, 100/240 Vac) |
|  |  | Nominal Voltage (Vac) | 100 | 120 | 200-240 |
|  |  | Voltage Range (Vac) (temporary condition) | 90-100 | 110-128 | 180-250 |
|  |  | Power Source Phase | Single | Single | Single |
|  |  | Nominal Frequency (Hz) | 50/60 | 50/60 | 50/60 |
|  |  | Frequency Range (Hz) | 49 to 51/59 to 61 | 49 to 51/59 to 61 | 49 to 51/59 to 61 |
|  |  | RMS Current (maximum steady state) |  |  |  |
|  |  | Pedestal and Rackmount |  |  |  |
|  |  | Single power cord | 6.6A | 5.5A | 3.0A |
|  |  | Maximum VA | 780 | 765 | 730 |
|  |  | M-series Cabinet (configuration dependent) |  |  |  |
|  |  | Nominal voltage (Vac) | 100 | 120 | 220-240 |
|  |  | Each power cord | 24A | 24A | 16A |
|  |  | Power Cords |  |  |
|  |  | Pedestal | 1 (75 in / 190 cm) | IEC 320 C13 to NEMA 5-15 (N. America) or IEC 320 C13 to country-specific |
|  |  | Rackmount | 1 (14 ft 10 in / 452 cm) | IEC 320 C13 to NEMA 5-15 (N. America) or IEC 320 C13 to IEC 320 C14 (other countries) |
|  |  | Cabinet | 2 (10 ft 10 in / 330 cm) | 120V non-removable NEMA L5-30P or 200-240V non-removable IEC 309 |
|  |  | Regulatory |  |
|  |  | Agency Approvals | UL: Listed to UL1950 (3rd edition) |
|  |  |  | CSA: Certified to CAN/CSA-C22.2 No. 950-M95 |
|  |  |  | TUV: EN 60950/A4: 1997 VDE 0805 GS marked |
|  |  |  | FCC: Part 15.B Class A |
|  |  |  | CE: EN55022, EN50082 |
|  |  |  | VCCI Class II ITE |
|  |  |  | BCIQ: CISPR22, CNS13438 |
|  |  |  | C-Tick: CISPR22, AS/NZS 3548 |
|  |  | Reviewed to | AS/NZ 3260:1993 Australian/New Zealand Standard |
|  |  |  | EN 60950/A4: 1997 European Norm |
|  |  |  | IEC 950 (2nd edition, 3rd amend) |

Maximum operating temperature at sea level; reduce by 1.8(F (1(C) for each 600m (2,000 ft) above sea level.

Higher altitudes are possible if maximum operating temperature is reduced (see Temperature); other restrictions may apply such as maximum permissible altitude for hard drives.

Current values for specific configurations are available from Compaq, note that 1 B = 10 dBA.

# Text boxes

Operator Control Panel

Removable media bay

Combination CD-ROM/floppy drive

Hard disk drives

Power supplies

Ultra2 SCSI adapter

System motherboard

CPU modules

Server Management Module

At A Glance

AlphaServer DS20E systems include:

Alpha 21264 processor, 500 MHz or 667 MHz (dual processor capability)

4-MB level 2 writeback cache per 500 MHz processor or 8-MB L2 DDR cache per 667 MHz processor

ECC-protected memory bus and cache

256-MB, 512-MB, or 1-GB  SDRAM memory expandable to 4 GB

Five PCI and one shared PCI/ISA slot (six total slots)

Four hot swap hard disk drive bays

Internal mass storage capacity up to 72.8 GB

Integrated environmental server management module

Two 375-Watt hot pluggable power supplies with optional third for N+1 redundancy

Combo 24X CD-ROM Drive and 1.44-MB floppy disk drive

Protected by Compaq Services, including a three-year on-site limited warranty

Revision 2.4

March 28, 2000