Ashtech Professional Products

Firmware Release Notice		Reference Station Products

Date:		August 11, 1999

Product	CGRS

Subject: 	Version CD00 Firmware Release

Number:

Introduction:

CD00 is a no cost firmware upgrade for the CGRS receivers. It can be downloaded from Ashtech FTP site ftp://ftp.ashtech.com. The self-extracting ZIP file CD00.exe in the firmware/cgrs folder contains the CD00 firmware and loading instructions. This version of CGRS firmware works with CGHOSE.EXE version CGRSCD00 and CGREMOTE.EXE version CGRSCD00.

Fixes/Enhancements:

‘C’ option no longer required.

Comments and Known Problems:

Except as noted above, units currently using CC00 do not need to upgrade at this time.

This version of CGRS firmware works with CGHOSE.EXE version CGRSCD00 and CGREMOTE.EXE version CGRSCD00

The $PASHS,ANT command will only accept antenna height values up to 6.4 Meters. Antenna heights greater than 6.4 meters must be entered with the $PASHS,ANH command.

CGHOSE displays only the first 3 digits of the week number in the Display /erase files screen.

Known Incompatibilities:

Previous Versions of CGREMOTE and CGHOSE may be incompatible.